## Slide 1: Classification And Forwarding
Lesson 9

## Slide 2: Recall
Packet demultiplexing
  – Used with layered protocols
  – Packet proceeds through one layer at a time
  – On input, software in each layer chooses module at next higher layer
  – On output, type field in each header specifies encapsulation

## Slide 3: The Disadvantage Of Demultiplexing
Although it provides freedom to define and use arbitrary protocols without introducing transmission overhead, demultiplexing is inefficient because it imposes sequential processing among layers.

## Slide 4: Packet Classification
Alternative to demultiplexing
Designed for higher speed
Considers all layers at the same time
Linear in number of fields
Two possible implementations
  – Software
  – Hardware

## Slide 5: Example Classification
Classify Ethernet frames carrying traffic to Web server
Specify exact header contents in rule set
Example
  – Ethernet type field specifies IP
  – IP type field specifies TCP
  – TCP destination port specifies Web server

## Slide 6: Example Classification (continued)
Field sizes and values
  – 2-octet Ethernet type is 0800 16
  – 2-octet IP type is 6
  – 2-octet TCP destination port is 80

## Slide 7: Software Implementation Of Classification
Compare values in header fields
Conceptually a logical and of all field comparisons
Example
if ( (frame type == 0x0800) && (IP type == 6) && (TCP port == 80) )
declare the packet matches the classification;
else
declare the packet does not match the classification;

## Slide 8: Optimizing Software Classification
Comparisons performed sequentially
Can reorder comparisons to minimize effort

## Slide 9: Example Of Optimizing Software Classification
Assume
  – 95.0% of all frames have frame type 0800 16
  – 87.4% of all frames have IP type 6
  – 74.3% of all frames have TCP port 80
Also assume values 6 and 80 do not occur in corresponding positions in non-IP packet headers
Reordering tests can optimize processing time

## Slide 10: Example Of Optimizing Software Classification (continued)
if ( (TCP port == 80) && (IP type == 6) && (frame type == 0x0800) )
declare the packet matches the classification;
else
declare the packet does not match the classification;
At each step, test the field that will eliminate the most packets

## Slide 11: Note About Optimization
Although the maximum number of comparisons in a software classifier is fixed, the average number of comparisons is determined by the order of the tests; minimum comparisons result if, at each step, the classifier tests the field that eliminates the most packets.

## Slide 12: Hardware Implementation Of Classification
Can build special-purpose hardware
Steps
  – Extract needed fields
  – Concatenate bits
  – Place result in register
  – Perform comparison
Hardware can operate in parallel

## Slide 13: Special Cases Of Classification
Multiple categories
Variable-size headers
Dynamic classification

## Slide 14: In Practice
Classification usually involves multiple categories
Packets grouped together into flows
May have a default category
Each category specified with rule set

## Slide 15: Example Multi-Category Classification
Flow 1: traffic destined for Web server
Flow 2: traffic consisting of ICMP echo request packets
Flow 3: all other traffic (default)

## Slide 16: Rule Sets
Web server traffic
  – 2-octet Ethernet type is 0800 16
  – 2-octet IP type is 6
  – 2-octet TCP destination port is 80
ICMP echo traffic
  – 2-octet Ethernet type is 0800 16
  – 2-octet IP type is 1
  – 1-octet ICMP type is 8

## Slide 17: Software Implementation Of Multiple Rules
if (frame type != 0x0800) {
send frame to flow 3;
} else if (IP type == 6 && TCP destination port == 80) {
send packet to flow 1;
} else if (IP type == 1 && ICMP type == 8) {
send packet to flow 2;
} else {
send frame to flow 3;
}
Further optimization possible

## Slide 18: Variable-Size Packet Headers
Fields not at fixed offsets
Easily handled with software
Finite cases can be specified in rules

## Slide 19: Example Variable-Size Header: IP Options
Rule Set 1
  – 2-octet frame type field contains 0800 16
  – 1-octet field at the start of the datagram contains 45 16
  – 1-octet type field in the IP datagram contains 6
  – 2-octet field 22 octets from start of the datagram contains 80
Rule Set 2
  – 2-octet frame type field contains 0800 16
  – 1-octet field at the start of the datagram contains 46 16
  – 1-octet type field in the IP datagram contains 6
  – 2-octet field 26 octets from the start of datagram contains 80

## Slide 20: Effect Of Protocol Design On Classification
Fixed headers fastest to classify
Each variable-size header adds one computation step
In worst case, classification no faster than demultiplexing
Extreme example: IPv6

## Slide 21: Hybrid Classification
Combines hardware and software mechanisms
  – Hardware used for standard cases
  – Software used for exceptions
Note: software classifier can operate at slower rate

## Slide 22: Two Basic Types Of Classification
Static
  – Flows specified in rule sets
  – Header fields and values known a priori
Dynamic
  – Flows created by observing packet stream
  – Values taken from headers
  – Allows fine-grain flows
  – Requires state information

## Slide 23: Example Static Classification
Allocate one flow per service type
One header field used to identify flow
  – IP TYPE OF SERVICE (TOS)
Use DIFFSERV interpretation
Note: Ethernet type field also checked

## Slide 24: Example Dynamic Classification
Allocate flow per TCP connection
Header fields used to identify flow
  – IP source address
  – IP destination address
  – TCP source port number
  – TCP destination port number
Note: Ethernet type and IP type fields also checked

## Slide 25: Implementation Of Dynamic Classification
Usually performed in software
State kept in memory
State information created/ updated at wire speed

## Slide 26: Two Conceptual Bindings
classification: packet flow
forwarding: flow packet disposition
Classification binding is usually 1-to-1
Forwarding binding can be 1-to-1 or many-to-1

## Slide 27: Flow Identification
Connection-oriented network
  – Per-flow SVC can be created on demand
  – Flow ID equals connection ID
Connectionless network
  – Flow ID used internally
  – Each flow ID mapped to ( next hop, interface )

## Slide 28: Relationship Of Classification And Forwarding In A Connection-Oriented Network
In a connection-oriented network, flow identifiers assigned by classification can be chosen to match connection identifiers used by the underlying network. Doing so makes forwarding more efficient by eliminating one binding.

## Slide 29: Forwarding In A Connectionless Network
Route for flow determined when flow created
Indexing used in place of route lookup
Flow identifier corresponds to index of entry in forwarding cache
Forwarding cache must be changed when route changes

## Slide 30: Second Generation Network Systems
Designed for greater scale
Use classification instead of demultiplexing
Decentralized architecture
  – Additional computational power on each NIC
  – NIC implements classification and forwarding
High-speed internal interconnection mechanism
  – Interconnects NICs
  – Provides fast data path

## Slide 31: Classification And Forwarding Chips
Sold by vendors
Implement hardware classification and forwarding
Typical configuration: rule sets given in ROM

## Slide 32: Summary
Classification faster than demultiplexing
Can be implemented in hardware or software
Dynamic classification
  – Uses packet contents to assign flows
  – Requires state information