## Slide 1: Microengine Programming II
Lesson 24

## Slide 2: Specialized Memory Operations
Buffer pool manipulation
Processor coordination via bit testing
Atomic memory increment
Processor coordination via memory locking

## Slide 3: Buffer Pool Manipulation
SRAM facility
Eight linked lists
Operations push and pop
General form of pop
sram [ pop, $xfer, – –, – –, listnum ]

## Slide 4: Processor Coordination Via Bit Testing
Provided by SRAM and Scratchpad memories
Atomic test-and-set
Mask used to specify bit in a word
General form
scratch [ bit_wr, $xfer, addr 1 , addr 2 , op ]

## Slide 5: Bit Manipulation Operations
Operation Meaning
set_bits Set the specified bits to one
clear_bits Set the specified bits to zero
test_and_set_bits Place the original word in the read transfer register, and set the specified bits to one
test_and_clear_bits Place the original word in the read transfer register, and set the specified bits to zero

## Slide 6: Atomic Memory Increment
Memory shared among
  – StrongARM
  – Microengines
Need atomic increment to avoid incorrect results
General form
scratch [ incr, – –, addr 1 , addr 2 , 1 ]

## Slide 7: Processor Coordination Via Memory Locking
Word of memory acts as mutual exclusion lock
Achieved with memory lock instruction
Single read_lock instruction
  – Obtains a lock on location X in memory
  – Reads values starting at location X
Single write_unlock instruction
  – Writes values to memory
  – Unlocks the specified location

## Slide 8: Processor Coordination Via Memory Locking (continued)
General form of read_lock
  sram [ read_lock, $xfer, addr 1 , addr 2 , count ], ctx_swap
Token ctx_swap required (thread blocks until lock obtained)
General form of write_unlock
sram [ unlock, – –, addr 1 , addr 2 , 1 ]

## Slide 9: Implementation Of Memory Locking
Achieved with a CAM that holds eight items
Only releases contiguous items in CAM
Consequences
  – At most eight addresses can be locked at any time
  – Thread can remained blocked even if its request can be satisfied

## Slide 10: Control And Status Registers
Over one hundred fifty
Provide access to hardware units on the chip
Allow processors to
  – Configure
  – Control
  – Interrogate
  – Monitor
Access
  – StrongARM: mapped into address space
  – Microengines: special instructions

## Slide 11: Csr Instruction
Used on microengines
General form
csr [ cmd, $xfer, CSR, count ]
Alternatives
  – Instruction fast_wr provides access to subset of CSRs through the FBI unit
  – Instruction local_csr_rd provides access to local CSRs

## Slide 12: Intel® Dispatch Loop Macros
Each microengine executes event loop
  – Analogous to core event loop
  – Events are low level (e.g., hardware device becomes ready)
  – Known as dispatch loop
SDK includes predefined macros related to dispatch loop

## Slide 13: Predefined Dispatch Loop Macros
Macro Purpose
Buf_Alloc Allocate a packet buffer
Buf_GetData Get the SDRAM address of a packet buffer
(note: the name is misleading)
DL_Drop Drop a packet and recycle the buffer
DL_GetBufferLength Compute the length (in bytes) of the packet portion of a buffer
DL_GetBufferOffset Compute the offset of packet data within a buffer
DL_GetInputPort Obtain the input port over which the packet arrived
DL_GetOutputPort Find the port over which the packet will be sent
DL_GetRxStat Obtain the receive status of the packet
DL_Init Initialize the dispatch loop macros
DL_MESink Send a packet to next microblock group
DL_SASink Send a packet to the StrongARM
DL_SASource Receive a packet from the StrongARM
DL_SetAceTag Specify the microblock that is handling a packet so the StrongARM wil know
DL_SetBufferLength Specify the length of packet data in the buffer
DL_SetBufferOffset Specify the offset of packet data in the buffer
DL_SetExceptionCode Specify the exception code for the StrongARM
DL_SetInputPort Specify the port over which the packet arrived
DL_SetOutputPort Specify the port on which the packet will be sent
DL_SetRxStat Specify the receive status of the packet

## Slide 14: Packet Selection Macros
Also supplied by SDK
Allow selection of packet from queues
Two approaches
  – Round-robin from a set of queues
    Used for 10 / 100 Ethernet
    Macro is RoundRobinSource
  – Strict FIFO ordering
    Used for Gigabit Ethernet
    Macro is FifoSource

## Slide 15: Obtaining Packets From StrongARM
Microengine can receive packets from
  – Input port (ingress) or another microengine
  – StrongARM
Dispatch loop tests for each possibility
Packets from StrongARM should have lower priority

## Slide 16: Implementation Of Priority
Macro EthernetIngress obtains Ethernet frame
Macro DL_SASource obtains packet from StrongARM
Each returns IX_BUFFER_NULL, if no packet waiting
To achieve priority, DL_SASource counts
SA_CONSUME_NUM times before returning a packet

## Slide 17: Packet Disposition
Auxiliary variable used
Dispatch loop finds a packet and calls macro X to process
Macro X sets variable dl_buffer_next
Dispatch loop examines dl_buffer_next and invokes
  – DL_Drop to drop packet
  – DL_SASink to send to StrongARM
  – DL_MESink to send to ‘‘next’’ ACE

## Slide 18: Other Predefined Macros
Macros needed for
  – Buffer manipulation
  – Packet processing
  – Other tasks
Predefined macros available

## Slide 19: Example Code To Process Packet Header
/* Allocate eight SDRAM transfer registers to hold the packet header */
xbuf_alloc [ $$hdr, 8 ]
/* Reserve two general-purpose registers for the computation */
.local base offset
/* Compute the SDRAM address of the data buffer */
Buf_GetData [ base, dl_buffer_handle ]
/* Compute the byte offset of the start of the packet in the buffer */
DL_GetBufferOffset [ offset ]
/* Convert the byte offset to SDRAM words by dividing by eight */
/* (shift right by three bits) */
alu_shf [ offset, – –, B, offset, >>3 ]
/* Load thirty-two bytes of data from SDRAM into eight SDRAM */
/* transfer registers. Start at SDRAM address base + offset */
sdram [ read, $$hdr0, base, offset, 4 ]

## Slide 20: Example Code To Process Packet Header (continued)
/* Inform the assembler that we have finished using the two */
/* registers: base and offset */
.endlocal
/* Process the packet header in the SDRAM transfer registers
/* starting at register $$hdr */
. . .
/* Free the SDRAM transfer registers when finished */
xbuf_free [ $$hdr ]

## Slide 21: Using Intel® Dispatch Macros
Programmer must perform five steps
  – Define three symbolic constants
  – Declare registers with a .local directive
  – Use a .import_var directive to name tag values (optional)
  – Include the macros pertinent to the microblock
  – Initialize the macros as the first part of a dispatch loop
Note: three constants must be defined before macros are included
  – SA_CONSUME_NUM
  – IX_EXCEPTION
  – SEQNUM_IGNORE

## Slide 22: Required Register Declarations
The following declarations are required
.local dl_reg1 dl_reg2 dl_reg3 dl_buffer_handle dl_next_block

## Slide 23: Naming Tag Values
Required in microblock that sends packets (exceptions) to core component
Uses .import_var directive
Example
.import_var IPV4_TAG

## Slide 24: Including Intel® Macros
Must include two files
  – DispatchLoop_h.uc
  – DispatchLoopImportVars.h
Ingress microblock includes
  – EthernetIngress.uc
Egress microblock includes
  – EthernetEgress.uc

## Slide 25: Initialization Of Intel® Macros
Program calls DL_Init to perform initialization
Typical initialization sequence
  DL_Init [ ]
  EthernetIngress_Init [ ]
  . . . /* Other microblock initialization calls */

## Slide 26: Packet I/ O
Physical frame divided into sixty-four octet units for transfer
Each unit known as mpacket
Division performed by interface hardware
Microengine transfers each mpacket separately
Header uses two bits to specify position of mpacket
  – Start Of Packet (SOP) set for first mpacket of frame
  – End Of Packet (EOP) set for last mpacket of frame
Note: cell can have both SOP and EOP set

## Slide 27: Packet I/ O (continued)
No interrupts
Dispatch loop uses polling
  – Ready Bus Sequencer checks devices and sets bit
  – Dispatch loop tests bit

## Slide 28: Ingress Packet Transfer
Incoming mpacket placed in Receive FIFO (RFIFO)
Microengine can transfer from RFIFO to
  – SRAM transfer registers
  – Directly into SDRAM
SDRAM transfer has form
sdram [ r_fifo_rd, $$xfer, addr 1 , addr 2 , count ], indirect_ref

## Slide 29: Packet Egress
Steps required
  – Reserve space in Transmit FIFO (TFIFO)
  – Copy mpacket from memory into TFIFO
  – Set SOP and EOP bits
  – Set valid flag in XMIT_VALIDATE register
General form used to copy from SDRAM to TFIFO
sdram [ t_fifo_wr, $$xfer, addr 1 , addr 2 , count ], indirect_ref

## Slide 30: Setting The Valid Flag In A XMIT_VALIDATE Register
Valid bit is in CSR
Use fast_wr instruction to access
fast_wr [ 0, xmit_validate ], indirect_ref

## Slide 31: Other Details
Microengine must check status of mpacket to determine if
  – MAC hardware detected problem (e.g., bad CRC)
  – Mpacket arrived with no problems
Information found in RCV_CNTL CSR

## Slide 32: Summary
Special operations used for
  – Synchronization
  – Memory access
  – CSR access
Microengine executes event loop known as dispatch loop
  – Checks for packets arriving
  – Calls macro(s) to process each packet
  – Sends packets to next specified destination
Intel® supplies large set of dispatch loop macros

## Slide 33: Summary (continued)
Many details required to use Intel® dispatch macros
Packet I/ O performed on sixty-four byte units called
mpackets
Mpacket can be transferred from RFIFO to
  – SRAM transfer registers
  – SDRAM
Many details required to perform trivial operations on packet