## Slide 1: Conventional Computer Hardware Architecture
Lesson 4

## Slide 2: Software-Based Network System
Uses conventional hardware (e.g., PC)
Software
  Runs the entire system
  Allocates memory
  Controls I/O devices
  Performs all protocol processing

## Slide 3: Why Study Protocol Processing On Conventional Hardware?
Past
  Employed in early IP routers
  Many algorithms developed / optimized for conventional hardware
Present
  Used in low-speed network systems
  Easiest to create / modify
  Costs less than special-purpose hardware

## Slide 4: Why Study Protocol Processing On Conventional Hardware? (continued)
Future
  Processors continue to increase in speed
  Some conventional hardware present in all systems

## Slide 5: Serious Question
Which is growing faster?
  Processing power
  Network bandwidth
Note: if network bandwidth growing faster
  Need special-purpose hardware
  Conventional hardware will become irrelevant

## Slide 6: Conventional Computer Hardware
Four important aspects
  Processor
  Memory
  I/O interfaces
  One or more buses

## Slide 7: Conventional Computer Architecture
Bus is central, shared interconnect
All components contend for use

## Slide 8: Bus Organization And Operations
Parallel wires (K+N+C total)
Used to pass
  An address of K bits
  A data value of N bits (width of the bus)
  Control information of C bits

## Slide 9: Bus Width
Wider bus
  Transfers more data per unit time
  Costs more
  Requires more physical space
Compromise: to simulate wider bus, use hardware that multiplexes transfers

## Slide 10: Bus Paradigm
Only two basic operations
  Fetch
  Store
All operations cast as forms of the above

## Slide 11: Fetch/Store
Fundamental paradigm
Used throughout hardware, including network processors

## Slide 12: Fetch Operation
Place address of a device on address lines
Issue fetch on control lines
Wait for device that owns the address to respond
If successful, extract value (response) from data lines

## Slide 13: Store Operation
Place address of a device on address lines
Place value on data lines
Issue store on control lines
Wait for device that owns the address to respond
If unsuccessful, report error

## Slide 14: Example Of Operations Mapped Into Fetch/Store Paradigm
Imagine disk device attached to a bus
Assume the hardware can perform three (nontransfer) operations:
  Start disk spinning
  Stop disk
  Determine current status

## Slide 15: Example Of Operations Mapped Into Fetch/Store Paradigm
Assign the disk two contiguous bus addresses D and D+1
Arrange for store of nonzero to address D to start disk spinning
Arrange for store of zero to address D to stop disk
Arrange for fetch from address D+1 to return current status
Note: effect of store to address D+1 can be defined as
  Appears to work, but has no effect
  Returns an error

## Slide 16: Bus Address Space
Arbitrary hardware can be attached to bus
K address lines result in 2k possible bus addresses
Address can refer to
  Memory (e.g., RAM or ROM)
  I/O device
Arbitrary devices can be placed at arbitrary addresses
Address space can contain ‘‘holes’’

## Slide 17: Bus Address Terminology
Device on bus known as memory mapped I/O
Locations that correspond to nontransfer operations known as Control and Status Registers (CSRs)

## Slide 18: Network I/O On Conventional Hardware
Network Interface Card (NIC)
  Attaches between bus and network
  Operates like other I/O devices
  Handles electrical/optical details of network
  Handles electrical details of bus
  Communicates over bus with CPU or other devices

## Slide 19: Making Network I/O Fast
Key idea: migrate more functionality onto NIC
Four techniques used with bus
  Onboard address recognition & filtering
  Onboard packet buffering
  Direct Memory Access (DMA)
  Operation and buffer chaining

## Slide 20: Onboard Address Recognition And Filtering
NIC given set of addresses to accept
  Station’s unicast address
  Network broadcast address
  Zero or more multicast addresses
When packet arrives, NIC checks destination address
  Accept packet if address on list
  Discard others

## Slide 21: Onboard Packet Buffering
NIC given high-speed local memory
Incoming packet placed in NIC’s memory
Allows computer’s memory/bus to operate slower than network
Handles small packet bursts

## Slide 22: Direct Memory Access (DMA)
CPU
  Allocates packet buffer in memory
  Passes buffer address to NIC
  Goes on with other computation
NIC
  Accepts incoming packet from network
  Copies packet over bus to buffer in memory
  Informs CPU that packet has arrived

## Slide 23: Buffer Chaining
CPU
  Allocates multiple buffers
  Passes linked list to NIC
NIC
  Receives next packet
  Divides into one or more buffers
Advantage: a buffer can be smaller than packet

## Slide 24: Operation Chaining
CPU
  Allocates multiple buffers
  Builds linked list of operations
  Passes list to NIC
NIC
  Follows list and performs instructions
  Interrupts CPU after each operation
Advantage: multiple operations proceed without CPU intervention

## Slide 25: Summary
Software-based network systems run on conventional hardware
  Processor
  Memory
  I/O Devices
  Bus
Network interface cards can be optimized to reduce CPU load