## Slide 1: Design Tradeoffs And Consequences
Lesson 16

## Slide 2: Low Development Cost Vs. Performance
The fundamental economic motivation
ASIC costs $1M to develop
Network processor costs programmer time

## Slide 3: Programmability Vs. Processing Speed
Programmable hardware is slower
Flexibility costs...

## Slide 4: Speed Vs. Functionality
Generic idea:
  – Processor with most functionality is slowest
  – Adding functionality to NP lowers its overall ‘‘speed’’

## Slide 5: Speed
Difficult to define
Can include
  – Packet Rate
  – Data Rate
  – Burst size

## Slide 6: Per-Interface Rates Vs. Aggregate Rates
Per-interface rate important if
  – Physical connections form bottleneck
  – System scales by having faster interfaces
Aggregate rate important if
  – Fabric forms bottleneck
  – System scales by having more interfaces

## Slide 7: Increasing Processing Speed Vs. Increasing Bandwidth
Will network processor capabilities or the bandwidth of network connections increase more rapidly?
What is the effect of more transistors?
Does Moore’s Law apply to bandwidth?

## Slide 8: Lookaside Coprocessors Vs. Flow-Through Coprocessors
Flow-through pipeline
  – Operates at wire speed
  – Difficult to change
Lookaside
  – Modular and easy to change
  – Invocation can be bottleneck

## Slide 9: Uniform Pipeline Vs. Synchronized Pipeline
Uniform pipeline
  – Operates in lock-step like assembly line
  – Each stage must finish in exactly the same time
Synchronized pipeline
  – Buffers allow computation at each stage to differ
  – Synchronization expensive

## Slide 10: Explicit Parallelism Vs. Cost And Programmability
Explicit parallelism
  – Hardware is less complex
  – More difficult to program
Implicit parallelism
  – Easier to program
  – Slightly lower performance

## Slide 11: Parallelism Vs. Strict Packet Ordering
Increased parallelism
  – Improves performance
  – Results in out-of-order packets
Strict packet ordering
  – Aids protocols such as TCP
  – Can nullify use of parallelism

## Slide 12: Stateful Classification Vs. High-Speed Parallel Classification
Static classification
  – Keeps no state
  – Is the fastest
Dynamic classification
  – Keeps state
  – Requires synchronization for updates

## Slide 13: Memory Speed Vs. Programmability
Separate memory banks
  – Allow parallel accesses
  – Yield high performance
  – Difficult to program
Non-banked memory
  – Easier to program
  – Lower performance

## Slide 14: I/ O Performance Vs. Pin Count
Bus width
  – Increase to produce higher throughput
  – Decrease to take fewer pins

## Slide 15: Programming Languages
A three-way tradeoff
Can have two, but not three of
  – Ease of programming
  – Functionality
  – Performance

## Slide 16: Programming Languages That Offer High Functionality
Ease of programming vs. speed
  – High-level language offers ease of programming, but lower performance
  – Low-level language offers higher performance, but makes programming more difficult

## Slide 17: Programming Languages That Offer Ease Of Programming
Speed vs. functionality
  – For restricted language, compiler can generate optimized code
  – Broad functionality and ease of programming lead to inefficient code

## Slide 18: Programming Languages That Offer High Performance
Ease of programming vs. functionality
  – Optimizing compiler and ease of programming imply a restricted application
  – Optimizing code for general applications requires more programmer effort

## Slide 19: Multithreading: Throughput Vs. Ease Of Programming
Multiple threads of control can increase throughput
Planning the operation of threads that exhibit less contention requires more programmer effort

## Slide 20: Traffic Management Vs. High-Speed Forwarding
Traffic management
  – Can manage traffic on multiple, independent flows
  – Requires extra processing
Blind forwarding
  – Performed at highest speed
  – Does not distinguish among flows

## Slide 21: Generality Vs. Specific Architectural Role
General-purpose network processor
  – Used in any part of any system
  Used with any protocol
  – More expensive
Special-purpose network processor
  – Restricted to one role / protocol
  – Less expensive, but may need many types

## Slide 22: Special-Purpose Memory Vs. General-Purpose Memory
General-purpose memory
  – Single type of memory serves all needs
  – May not be optimal for any use
Special-purpose memory
  – Optimized for one use
  – May require multiple memory types

## Slide 23: Backward Compatibility Vs. Architectural Advances
Backward compatibility
  – Keeps same instruction set through multiple versions
  – May not provide maximal performance
Architectural advances
  – Allows more optimizations
  – Difficult for programmers

## Slide 24: Parallelism Vs. Pipelining
Both are fundamental performance techniques
Usually used in combination: pipeline of parallel processors
  – How long is pipeline?
  – How much parallelism at each stage?

## Slide 25: Summary
Many design tradeoffs
No easy answers