## Slide 1: Basic Terminology And Example Systems (A Quick Review)
Lesson 2

## Slide 2: Packets Cells And Frames
Packet
  Generic term
  Small unit of data being transferred
  Travels independently
  Upper and lower bounds on size

## Slide 3: Packets Cells And Frames (continued)
Cell
  Fixed-size packet (e.g., ATM)
Frame or layer-2 packet
  Packet understood by hardware
IP datagram
  Internet packet

## Slide 4: Types Of Networks
Paradigm
  Connectionless
  Connection-oriented
Access type
  Shared (i.e., multiaccess)
  Point-To-Point

## Slide 5: Point-To-Point Network
Connects exactly two systems
Often used for long distance
Example: data circuit connecting two routers

## Slide 6: Data Circuit
Leased from phone company
Also called serial line because data is transmitted bit-serially
Originally designed to carry digital voice
Cost depends on speed and distance
T-series standards define low speeds (e.g. T1)
STS and OC standards define high speeds

## Slide 7: Local Area Networks
Ethernet technology dominates
Layer 1 standards
  Media and wiring
  Signaling
  Handled by dedicated interface chips
  Unimportant to us
Layer 2 standards
  MAC framing and addressing

## Slide 8: MAC Addressing
Three address types
  Unicast (single computer)
  Broadcast (all computers in broadcast domain)
  Multicast (some computers in broadcast domain)

## Slide 9: More Terminology
Internet
  Interconnection of multiple networks
  Allows heterogeneity of underlying networks
Network scope
  Local Area Network (LAN) covers limited distance
  Wide Area Network (WAN) covers arbitrary distance

## Slide 10: Network System
Individual hardware component
Serves as fundamental building block
Used in networks and internets
May contain processor and software
Operates at one or more layers of the protocol stack

## Slide 11: Example Network Systems
Layer 2
  Bridge
  Ethernet switch
  VLAN switch

## Slide 12: VLAN Switch
Similar to conventional layer 2 switch
  Connects multiple computers
  Forwards frames among them
  Each computer has unique unicast address
Differs from conventional layer 2 switch
  Allows manager to configure broadcast domains
Broadcast domain known as virtual network

## Slide 13: Broadcast Domain
Determines propagation of broadcast / multicast
Originally corresponded to fixed hardware
  One per cable segment
  One per hub or switch
Now configurable via VLAN switch
  Manager assigns ports to VLANs

## Slide 14: Example Network Systems (continued)
Layer 3
  Internet host computer
  IP router (layer 3 switch)
Layer 4
  Basic Network Address Translator (NAT)
  Round-robin Web load balancer
  TCP terminator

## Slide 15: Example Network Systems (continued)
Layer 5
  Firewall
  Intrusion Detection System (IDS)
  Virtual Private Network (VPN)
  Softswitch running SIP
  Application gateway
  TCP splicer (also known as NAPT — Network Address and Protocol Translator)
  Smart Web load balancer
  Set-top box

## Slide 16: Example Network Systems (continued)
Network control systems
  Packet / flow analyzer
  Traffic monitor
  Traffic policer
  Traffic shaper