## Slide 1: Reference System And Software Development Kit (Bridal Veil, SDK)
Lesson 20

## Slide 2: Reference System
Provided by vendor
Targeted at potential customers
Usually includes
  – Hardware testbed
  – Development software
  – Download and bootstrap software
  – Reference implementations

## Slide 3: Intel Reference Hardware
Single-board network processor testbed
Plugs into PCI bus on a PC

## Slide 4: Intel Reference Hardware (continued)
Quantity or Size Item
1 Intel® IXP1200 network processor (232MHz)
8 Mbytes of SRAM memory
256 Mbytes of SDRAM memory
8 Mbytes of Flash ROM memory
4 10/ 100 Ethernet ports
1 Serial interface (console)
1 PCI bus interface
1 PMC expansion site

## Slide 5: Intel Reference Software
Known as Software Development Kit (SDK)
Runs on PC
Includes:
Software Purpose
C compiler Compile programs for the StrongARM
MicroC compiler Compile programs for the microengines
Assembler Assemble programs for the microengines
Downloader Load software into the network processor
Monitor Communicate with the network processor and
interact with running software
Bootstrap Start the network processor running
Reference Code Example programs for the Intel® IXP1200 that show
how to implement basic functions

## Slide 6: Basic Paradigm
Build software on conventional computer
Load into reference system
Test / measure results

## Slide 7: Bootstrapping Procedure
Powering on host causes network processor board to run boot monitor from Flash memory
Device driver on host communicates across the PCI bus with bootmonitor to load operating system (Embedded Linux) and initial RAM disk configuration into network processor’s memory
Host signals boot monitor to start the StrongARM
Operating system runs login process on serial line and starts telnet server
Operating systems on host and StrongARM configure PCI bus to act as Ethernet emulator; the StrongARM uses NFS to mount two file systems, R and W, from a server on the host

## Slide 8: Starting Software
Compile code for StrongARM and microengines
Create system configuration file named ixsys.config
Copy code and configuration file to read-only public download directory, R
Run terminal emulation program on host and log onto StrongARM
Change to NSF-mounted directory R, and run shell script ixstart with argument ixsys.config
Later, to stop the Intel® IXP1200, run ixstop script

## Slide 9: Summary
Reference systems
  – Provided by vendor
  – Targeted at potential customers
  – Usually include
    Hardware testbed
    Cross-development software
  Download and bootstrap software
  Reference implementations