## Slide 1: Languages Used For Classification
Lesson 15

## Slide 2: Languages For Building A Network Stack
Many questions
  – What language(s) are best?
  – How should processing be expressed?
  – How important is efficiency?
  – Must code be optimized by hand?

## Slide 3: Possible Programming Paradigms
Declarative
Imperative
  – With explicit parallelism
  – With implicit parallelism

## Slide 4: Choices Depend On
Underlying hardware architecture
Data and packet rates
Software support available (e.g., compilers)

## Slide 5: Desiderata
High-level
Declarative
Data-oriented
Efficient
General or extensible
Explicit links to actions

## Slide 6: Possible Hardware Architectures
RISC processor dedicated to classification
RISC processor shared with other tasks
Multiple, parallel RISC processors
State machine or FPGA

## Slide 7: Example Classification Languages
We will consider two examples
  – NCL
  – FPL

## Slide 8: NCL
Expands to Network Classification Language
Developed by Intel
Runs on StrongARM
Not part of fast path

## Slide 9: NCL
Network Classification Language
Developed by Intel
Runs on StrongARM
Not part of fast path

## Slide 10: NCL Characteristics
High level
Mixes declarative and imperative paradigms
Associates action with each classification
Optimized for protocols with fixed-size header fields
Basic unit of data is eight-bit byte

## Slide 11: NCL Notation
Item specified by tuple
  – Offset beyond a base
  – Size
Syntax:
base [ offset : size ]
Example
– Two-octet field fourteen octets beyond symbol FRAME
FRAME [ 14 : 2 ]

## Slide 12: NCL Measures Of Data Size
Octets
  – Default
  – Syntax consists of integers
  – Usually more efficient

## Slide 13: NCL Measures Of Data Size (continued)
Bits
  – Can specify arbitrary bit position / length
  – Syntax uses less-than and greater-than
  – Usually less efficient
  – Example of a four-bit string six bits beyond FRAME
FRAME [ <6> : <4> ]

## Slide 14: NCL Comments
C-style
/* ... */
C++-style
// ...

## Slide 15: NCL Primitives
Can name header fields
Names defined by offset / length
No predefined protocol specifications
  – NCL does not understand IP, TCP, Ethernet, etc.
No predefined network data types
  – NCL does not understand IP addresses, Ethernet addresses, etc.

## Slide 16: Example NCL Code
protocol ip { /* declaration of datagram header */
vershl { ip[0:1] }
vers { ( vershl & 0xf0 ) >> 4 }
tmphl { ( vershl & 0x0f ) }
hlen { tmphl << 2 }
totlen { ip[2:2] }
ident { ip[4:2] }
frags { ip[6:2] }
ttl { ip[8:1] }
proto { ip[9:1] }
cksum { ip[10:2] }
source { ip[12:4] }
dest { ip[16:4] }
demux {
( proto == 6 ) { tcp at hlen }
( proto == 17 ) { udp at hlen }
( default ) { ipunknown at hlen }
// note: other protocol types can be added here
}
} // end of datagram header declaration

## Slide 17: IP Header Length
Found in second four bits of IP header
Gives header size in 32-bit multiples
NCL can
  – Define fields on byte boundaries
  – Extract bit fields
  – Perform basic arithmetic

## Slide 18: Example NCL Code To Extract Header Length
vershl { ip[0:1] }
vers { ( vershl & 0xf0 ) >> 4 }
tmphl { ( vershl & 0x0f ) }
hlen { tmphl << 2 }

## Slide 19: Encapsulation
Needed for layered protocols
Type field from layer N specifies type of message encapsulated at layer N + 1
Specified using at keyword

## Slide 20: Example NCL Code For Encapsulation
( proto == 6 ) { tcp at hlen }
( proto == 17 ) { udp at hlen }
( default ) { ipunknown at hlen }
If IP protocol is 6, tcp
If IP protocol is 17, icmp
Other cases classified as ipunknown

## Slide 21: Actions
Refers to imperative execution
Names function to execute
Associated with each classification
Specified by rule statement

## Slide 22: Example NCL Code To Invoke An Action
rule web_filter { ip && tcp.dport == 80 } { web_proc(ip.src) }
Specifies
  – Name is web_filter
  – Predicate is ip && tcp.dport == 80
  – Action to be invoked is web_proc(ip.src)

## Slide 23: Intrinsic Functions
Built into language
Handle checksum
  – Verification
  – Calculation
Understand specific protocols

## Slide 24: Available Intrinsic Functions
Function Name Purpose
ip.chksumvalid Verifies validity of IP checksum
ip.genchksum Generates an IP checksum
tcp.chksumvalid Verifies validity of TCP checksum
tcp.genchksum Generates a TCP checksum
udp.chksumvalid Verifies validity of UDP checksum
udp.genchksum Generates a UDP checksum

## Slide 25: Named Predicates
Bind name to predicate
Can be used later in program
Associated with specific protocol

## Slide 26: Example Predicate
predicate ip.fragmentable { ! ( (ip.frags >> 14) & 0x01 ) }

## Slide 27: Conditional Rule Execution
Specifies order for predicate testing
Linearizes classification
Helps optimize processing
Example use: verify IP checksum before proceeding

## Slide 28: Illustration Of NCP Conditional Rule Execution
predicate TCPvalid { tcp && tcp.cksumvalid }
with { ( TCPvalid ) {
predicate SynFound { (tcp.flags & 0x02) }
rule NewConnection { SynFound } { start_conn(tcp_dport) }
}

## Slide 29: Incremental Protocol Definition
Allows programmer to add definition of field to pre-existing protocol specification
Works well with included files
Useful when generic definition insufficient
General form:
field protocol_name.field_name { definition }
Example
field ip.flags { ip[6 : <3>] }

## Slide 30: NCL Set Facility
Table search mechanism
Tables grow dynamically
Up to seven keys (each key is 32-bits)
Programmer gives table size
  – Size must be power of two
  – Set can grow larger than estimate

## Slide 31: Example NCL Set Declaration
To declare set my_addrs:
set my_addrs /* define a set of IP addresses */
< 1 > { /* number of keys in each entry */
size_hint { 256 }
}

## Slide 32: Example NCL Set Declaration (continued)
To search my_addrs:
search my_addrs. ip_src_lookup
(ip.source) /* search key is IP source addr. */

## Slide 33: NCL Preprocessor
Adopts syntax from C-preprocessor
Provides
  – #include
  – #ifndef

## Slide 34: FPL
Functional Programming Language
Developed by Agere Systems*
Runs on Agere Systems* FPP
In the fast path

## Slide 35: FPL Characteristics
High level
Unusual, declarative language
Follows pattern paradigm
Designed for networking
Differs from conventional syntactic pattern languages like SNOBOL or Awk
Permits parallel evaluation

## Slide 36: FPL Syntax
C++ comments // I can’t understand this...
C-like preprocessor (#define)
Variety of constants
  – Decimal
  – Hexadecimal (begins with 0x)
  – Bit string (begins with 0b)
  – Dotted decimal IP addresses
  – Dashed hexadecimal addresses

## Slide 37: Two Pass Processing
Fundamental idea in FPL
Program contains two independent parts
Incoming data processed by both parts
Motivation: underlying interface hardware

## Slide 38: Interface Hardware
Divides each incoming packet into blocks of 64 octets
Transfers one block at a time to FPP chip
Sends additional information with each block
  – Port number on which received
  – Flags
    Hardware detected error (e.g., invalid CRC)
    Block is the first block of packet
    Block is the final block of packet

## Slide 39: Pass 1 Processing (blocks)
Program invoked once for each block
Accommodates blocks from multiple interfaces
Collects the blocks for each packet into a separate queue
Forwards complete queue to Pass 2 when
  – Final block of packet arrives
  – Error detected and processing aborted

## Slide 40: Pass 2 Processing (packets)
Program invoked once for each packet
Handles complete packet
Receives
  – Packet from Pass 1
  – Status information for the packet
Chooses disposition
  – Forward packet for transmission
  – Discard packet

## Slide 41: FPL Invocation
Handled by hardware
Pass 1 invoked when block arrives
Pass 2 invoked when packet ready
No explicit polling

## Slide 42: Designating Passes
Programmer specifies starting label for each pass
Handled by language directives
To designate first pass:
SETUP ROOT( starting_label )
To designate second pass:
SETUP REPLAYROOT( starting_label )

## Slide 43: Using A Pattern Match For Conditional Processing
Fact 1: FPL does not provide a conditional statement
Fact 2: FPL does provide matching among a set of patterns
Trick: use pattern selection to emulate conditional execution

## Slide 44: Example Conditional In First Pass Processing
Hardware sets variable $FramerEOF
  – Value is 1 if block is final block of packet
  – Value is 0 for other blocks
Built-in functions used to enqueue block
  – fQueue adds block to queue
  – fQueueEOF adds block to queue and marks queue ready for second pass

## Slide 45: Example Conditional In First Pass Processing (continued)
Conceptual algorithm for enqueuing a block:
if ( $FramerEOF ) {
fQueueEOF( );
} else {
fQueue( );
}

## Slide 46: Pattern Used For Conditional
#include "fpp.fpl"
// Code for the first pass of a program that handles Ethernet packets
SETUP ROOT(HandleBlock);
// Pass 1
HandleBlock: EtherBlock($framerEOF:1);
EtherBlock: 0b0 fQueue(0:2, $portNumber:16, $offset:6, 0:1, 0:2);
EtherBlock: 0b1 fQueueEof(0:2, $portNumber:16, $offset:6, 0:1, 0:2, 0:24);

## Slide 47: Code For Second Pass
// Code for the second pass of a program that classifies Ethernet frames
// Symbolic constants used for classifications
#define FRAMETYPEA 1 // ARP frames
#define FRAMETYPEI 2 // IP frames
#define FRAMETYPEO 3 // Other frames (not the above)
SETUP REPLAYROOT(HandleFrame);
// Pass 2
HandleFrame:
fSkip(96) // skip past dest & src addresses
cl = CLASS // compute class from frame type
fSkipToEnd()
fTransmit(cl:21, 0:16, 0:5, 0:6);
CLASS: 0x0806:16 fReturn(FRAMETYPEA);
CLASS: 0x0800:16 fReturn(FRAMETYPEI);
CLASS: BITS:16 fReturn(FRAMETYPEO);

## Slide 48: Conceptual Pattern Match
Program specifies sequence of patterns
Pointer moves through packet
Processing proceeds if bits in packet match pattern

## Slide 49: Two Basic Types Of Pattern Functions
Control function
  – Sequence of items to match
  – Processed in order
  – Exactly one path
Tree function
  – Set of patterns
  – Data in packet compared to all patterns
  – Exactly one must match

## Slide 50: Example Control Function
HandleFrame:
fSkip(96) // skip past dest & src addresses
cl = CLASS // compute class from frame type
fSkipToEnd()
fTransmit(cl:21, 0:16, 0:5, 0:6);

## Slide 51: Example Tree Function
CLASS:0x0806:16 fReturn(FRAMETYPEA);
CLASS:0x0800:16 fReturn(FRAMETYPEI);
CLASS:BITS:16 fReturn(FRAMETYPEO);

## Slide 52: Special Patterns
fSkip
  – Skips bits in input
fSkipToEnd
  – Skips to end of current packet
fTransmit
  – Sends packet to RSP chip
BITS
  – Matches arbitrary bits (default case)
Note: second pass must match entire packet

## Slide 53: Pattern Optimization
FPL compiler optimizes patterns
Typical optimization: eliminate common prefix

## Slide 54: Example Pattern Optimization
IP: 0x4 0x5 fSkip(152) fReturn(IPOPTIONS0);
IP: 0x4 0x6 fSkip(160) fReturn(IPOPTIONS1);
IP: 0x4 0x7 fSkip(168) fReturn(IPOPTIONS2);
IP: 0x4 BITS:4 fReturn(IPUNKNOWN);
(a)
IP: 0x4 IPHDR;
IPHDR: 0x5 fSkip(152) fReturn(IPOPTIONS0);
IPHDR: 0x6 fSkip(160) fReturn(IPOPTIONS1);
IPHDR: 0x7 fSkip(168) fReturn(IPOPTIONS2);
IPHDR: BITS:4 fReturn(IPUNKNOWN);
(b)

## Slide 55: IP Address Example
ipAddrMatch: *.*.*.* fReturn(0);
ipAddrMatch: 10.*.*.* fReturn(1);
ipAddrMatch: 128.10.*.* fReturn(2);
ipAddrMatch: 128.211.*.* fReturn(2);
ipAddrMatch: 128.210.*.* fReturn(3);

## Slide 56: Dynamic Classification
Can extend tree function at run-time
Requires use of ASI
Pattern converted to internal form

## Slide 57: Summary
Programming languages for classification are
  – Special-purpose
  – High-level
  – Declarative
  – Data-oriented
  – Provide links to actions
We examined two languages
  – NCL, the Network Classification Language from Intel Corporation
  – FPL, the Functional Programming Language from Agere Systems*