## Slide 1: Microengine Programming I
Lesson 23

## Slide 2: Microengine Code
Many low-level details
Close to hardware
Written in assembly language

## Slide 3: Features Of Intel’s Microengine Assembler
Directives to control assembly
Symbolic register names
Macro preprocessor (extension of C preprocessor)
Set of structured programming macros

## Slide 4: Statement Syntax
General form:
label: operator operands token
Interpretation of token depends on instruction

## Slide 5: Comment Statements
Three styles available
  – C style (between / * and */ )
  – C++ style ( / / until end of line )
  – Traditional assembly style ( ; until end of line )
Only traditional comments remain in code for intermediate steps of assembly

## Slide 6: Assembler Directives
Begin with period in column one
Can
  – Generate code
  – Control assembly process
Example: associate myname with register five in the A register bank
.areg myname 5

## Slide 7: Example Operand Syntax
Instruction alu invokes the ALU
alu [ dst, src 1 , op, src 2 ]
Four operands
  – Destination register
  – First source register
  – Operation
  – Second source register
Two minus signs ( – – ) can be specified for destination, if none needed

## Slide 8: Memory Operations
Programmer specifies
  – Type of memory
  – Direction of transfer
  – Address in memory (two registers used)
  – Starting transfer register
  – Count of words to transfer
  – Optional token

## Slide 9: Memory Operations (continued)
General forms
sram [ direction, xfer_reg, addr 1 , addr 2 , count ], optional_token
sdram [ direction, xfer_reg, addr 1 , addr 2 , count ], optional_token
scratch [ direction, xfer_reg, addr 1 , addr 2 , count ], optional_token

## Slide 10: Memory Addressing
Specified with operands addr 1 and addr 2
Each operand corresponds to register
Use of two operands allows
  – Base + offset
  – Scaling to large memory

## Slide 11: Immediate Instruction
Place constant in thirty-two bit register
immed [ dst, ival, rot ]
Upper sixteen bits of ival must be all zeros or all ones
Operand rot specifies bit rotation
0 No rotation
<< 0 No rotation (same as 0)
<< 8 Rotate to the left by eight bits
<< 16 Rotate to the left by sixteen bits

## Slide 12: Register Names
Usually automated by assembler
Directives available for manual assignment
Directive Type Of Register Assigned
.areg General-purpose register from the A bank
.breg General-purpose register from the B bank
.$reg SRAM transfer register
.$$reg SDRAM transfer register

## Slide 13: Automated Register Assignment
Programmer
  – Uses .local directive to declare register names
  – Uses .endlocal to terminate scope
  – References names in instructions
Assembler
  – Assigns registers
  – Chooses bank for each register
  – Replaces names in code with correct reference

## Slide 14: Illustration Of Automated Register Naming
One or more register names specified on .local
Example
  .local myreg loopctr tot
  // Code in this block can use registers myreg, loopctr, and tot
  .
  .
  .
  .endlocal
Names valid only within scope
Scopes can be nested

## Slide 15: Illustration Of Nested Register Scope
.local myreg loopctr // outer scope defines myreg & loopctr
.local rone rtwo // nested scope defines rone & rtwo
.
.
.
.endlocal
.local rthree rfour // nested scope defines rthree & rfour
.
.
.
.endlocal
.endlocal

## Slide 16: Conflicts
Operands must come from separate banks
Some code sequences cause conflict
    Example
    Z ← Q + R;
    Y ← R + S;
    X ← Q + S;
No assignment is valid
Programmer must change code

## Slide 17: Macro Preprocessor Features
File inclusion
Symbolic constant substitution
Conditional assembly
Parameterized macro expansion
Arithmetic expression evaluation
Iterative generation of code

## Slide 18: Macro Preprocessor Statements
Keyword Use
#include Include a file
#define Define symbolic constant
#define_eval Eval arithmetic expression & define constant
#undef Remove previous definition
#macro Start macro definition
#endm End a macro definition
#ifdef Start conditional compilation if defined
#ifndef Start conditional compilation if not defined
#if Start conditional compilation if expr. true
#else Else part of conditional compilation
#elif Else if part of conditional compilation
#endif End of conditional compilation
#for Start definite iteration
#while Start indefinite iteration
#repeat Start indefinite iteration (test after)
#endloop Terminate an iteration

## Slide 19: Macro Definition
Can occur at any point in program
General form:
  #macro name [ parameter 1 , parameter 2 , . . . ]
  lines of text
  #endm

## Slide 20: Macro Example
Compute a = b + c + 5
/* example macro add5 computes a=b+c+5 */
#macro add5[a, b, c]
.local tmp
alu[tmp, c, +, 5]
alu[a, b, +, tmp]
.endlocal
#endm
Assumes values a, b, and c in registers

## Slide 21: Macro Expansion Example
Call of add5[var1, var2, var3] expands to:
.local tmp
alu[tmp, var3, +, 5]
alu[var1, var2, +, tmp]
.endlocal
Warning: can generate illegal code

## Slide 22: Generation Of Repeated Code
Macro preprocessor
  – Supports #while statement for iteration
  – Uses #define_eval for arithmetic evaluation
Can be used to generate repeated code

## Slide 23: Example Of Repeated Code
Preprocessor code:
  #define LOOP 1
  #while (LOOP < 4)
    alu_shf[reg, -, B, reg, >>LOOP]
  #define_eval LOOP LOOP + 1
  #endloop
Expands to:
    alu_shf[reg, -, B, reg, >>1]
    alu_shf[reg, -, B, reg, >>2]
    alu_shf[reg, -, B, reg, >>3]

## Slide 24: Structured Programming Directives
Make code appear to follow structured programming conventions
Include break statement al la C
Directive Meaning
.if Conditional execution
.elif Terminate previous conditional execution and
start a new conditional execution
.else Terminate previous conditional execution and
define an alternative
.endif End .if conditional
.while Indefinite iteration with test before
.endw End .while loop
.repeat Indefinite iteration with test after
.until End .repeat loop
.break Leave a loop
.continue Skip to next iteration of loop

## Slide 25: Mechanisms For Context Switching
Context switching is voluntary
Thread can execute:
  – ctx_arb instruction
  – Reference instruction (e.g., memory reference)

## Slide 26: Argument To ctx_arb Instruction
Determines disposition of thread
  – voluntary: thread suspended until later
  – signal_event: thread suspended until specified event occurs
  – kill: thread terminated

## Slide 27: Context Switch On Reference Instruction
Token added to instruction to control context switch
Two possible values
  – ctx_swap: thread suspended until operation completes
  – sig_done: thread continues to run, and signal posted when operation completes
Signals available for SRAM, SDRAM, FBI, PCI, etc.

## Slide 28: Indirect Reference
Poor choice of name
Hardware optimization
Found on other RISC processors
Result of one instruction modifies next instruction
Avoids stalls
Typical use
  – Compute N, a count of words to read from memory
  – Modify memory access instruction to read N words

## Slide 29: Fields That Can Be Modified
Microengine associated with a memory reference
Starting transfer register
Count of words of memory to transfer
Thread ID of the hardware thread (i.e., thread to signal upon completion)

## Slide 30: How Indirect Reference Operates
Programmer codes two instructions
  – ALU operation
  – Instruction with indirect reference set
Note: destination of ALU operation is – – (i.e., no destination)
Hardware
  – Executes ALU instruction
  – Uses result of ALU instruction to modify field in next instruction

## Slide 31: Example Of Indirect Reference
Example code
    alu_shf [ – –, – –, b, 0x13, << 16 ]
    scratch [ read, $reg0, addr1, addr2, 0 ], indirect_ref
Memory instruction coded with count of zero
ALU instruction computes count

## Slide 32: Transfers
Microengine cannot directly access
  – Memory
  – Buses ( I/ O devices )
Intermediate hardware units used
  – Known as transfer registers
  – Multiple registers can be used as large, contiguous buffer

## Slide 33: External Transfer Procedure
Allocate contiguous set of transfer registers to hold data
Start reference instruction that moves data to or from allocated registers
Arrange for thread to wait until the operation completes

## Slide 34: Allocating Contiguous Registers
Registers assigned by assembler
Programmer needs to ensure transfer registers contiguous
Assembler provides .xfer_order directive
Example: allocate four continuous SRAM transfer registers
    .local $reg1 $reg2 $reg3 $reg4
    .xfer_order $reg1 $reg2 $reg3 $reg4

## Slide 35: Summary
Microengines programmed in assembly language
Intel’s assembler provides
  – Directives for structuring code
  – Macro preprocessor
  – Automated register assignment