## Slide 1: Review Of Protocols And Packet Formats
Lesson 3

## Slide 2: Protocol Layering
Application
Transport
Internet
Network Interface
Physical
Layer 5
Layer 4
Layer 3
Layer 2
Layer 1
Five-layer Internet Reference model
Multiple protocols can occur at each layer

## Slide 3: Layer 2 Protocols
Two protocols are important
  Ethernet
  ATM
We will concentrate on Ethernet

## Slide 4: Ethernet Addressing
48-bit addressing
Unique address assigned to each station (NIC)
Destination address in each packet can specify delivery to
  A single computer (unicast)
  All computers in broadcast domain (broadcast)
  Some computers in broadcast domain (multicast)

## Slide 5: Ethernet Addressing (continued)
Broadcast address is all 1s
Single bit determines whether remaining addresses are unicast or multicast

## Slide 6: Ethernet Frame Processing
6
6
2
46 - 1500
Destination Address
Source Address
Frame Type
Data in Frame
Header
Payload
Dedicated physical layer hardware
  Checks and removes preamble and CRC on input
  Computes and appends CRC and preamble on output
Layer 2 systems use source, destination and (possibly) type fields

## Slide 7: Internet
Set of (heterogeneous) computer networks interconnected by IP routers
End-user computers, called hosts, each attach to specific network
Protocol software
  Runs on both hosts and routers
  Provides illusion of homogeneity

## Slide 8: Internet Protocols Of Interest
Layer 2
  Address Resolution Protocol (ARP)
Layer 3
  Internet Protocol (IP)
Layer 4
  User Datagram Protocol (UDP)
  Transmission Control Protocol (TCP)