## Slide 1: Issues In Scaling A Network Processor
Lesson 14

## Slide 2: Design Questions
Can we make network processors
  – Faster?
  – Easier to use?
  – More powerful?
  – More general?
  – Cheaper?
  – All of the above?
Scale is fundamental

## Slide 3: Scaling The Processor Hierarchy
Make processors faster
Use more concurrent threads
Increase processor types
Increase numbers of processors

## Slide 4: The Pyramid Of Processor Scale
CPU
Embedded Proc.
I /O Processors
Lower Levels Of Processor Hierarchy
Lower levels need the most increase

## Slide 5: Scaling The Memory Hierarchy
Size
Speed
Throughput
Cost

## Slide 6: Memory Speed
Access latency
  – Raw read/ write access speed
  – SRAM 2 - 10 ns
  – DRAM 50 - 70 ns
  – External memory takes order of magnitude longer than onboard

## Slide 7: Memory Speed (continued)
Memory cycle time
  Measure of successive read/ write operations
  – Important for networking because packets are large
  – Read Cycle time (tRC) is time for successive fetch operations
  – Write Cycle time (tWC) is time for successive store operations

## Slide 8: The Pyramid Of Memory Scale
Largest memory is least expensive
Reg
Onboard mem.
External SRAM
External DRAM

## Slide 9: Memory Bandwidth
General measure of throughput
More parallelism in access path yields more throughput
Cannot scale arbitrarily
  – Pinout limits
  – Processor must have addresses as wide as bus

## Slide 10: Types Of Memory
Memory Technology Abbreviation Purpose
Synchronized DRAM SDRAM Synchronized with CPU
for lower latency
Quad Data Rate SRAM QDR-SRAM Optimized for low latency
and multiple access
Zero Bus Turnaround SRAM ZBT-SRAM Optimized for random
access
Fast Cycle RAM FCRAM Low cycle time optimized
for block transfer
Double Data Rate DRAM DDR-DRAM Optimized for low
latency
Reduced Latency DRAM RLDRAM Low cycle time and
low power requirements

## Slide 11: Memory Cache
General-purpose technique
May not work well in network systems

## Slide 12: Memory Cache
General-purpose technique
May not work well in network systems
  – Low temporal locality
  – Large cache size (either more entries or larger granularity of access)

## Slide 13: Content Addressable Memory (CAM)
Combination of mechanisms
  – Random access storage
  – Exact-match pattern search
Rapid search enabled with parallel hardware

## Slide 14: Lookup In Conventional CAM
Given
  – Pattern for which to search
  – Known as key
CAM returns
  – First slot that matches key, or
  – All slots that match key

## Slide 15: Ternary CAM (T-CAM)
Allows masking of entries
Good for network processor

## Slide 16: T-CAM Lookup
Each slot has bit mask
Hardware uses mask to decide which bits to test
Algorithm
  for each slot do {
  if ( ( key & mask ) == ( slot & mask ) ) {
  declare key matches slot;
  } else {
  declare key does not match slot;
  }
  }

## Slide 17: Using A T-CAM For Classification
Extract values from fields in headers
Form values in contiguous string
Use a key for T-CAM lookup
Store classification in slot

## Slide 18: Software Scalability
Not always easy
Many resource constraints
Difficulty arises from
  – Explicit parallelism
  – Code optimized by hand
  – Pipelines on heterogeneous hardware

## Slide 19: Summary
Scalability key issue
Primary subsystems affecting scale
  – Processor hierarchy
  – Memory hierarchy
Many memory types available
  – SRAM
  – SDRAM
  – CAM
T-CAM useful for classification