## Slide 1: Switching Fabrics
Lesson 10

## Slide 2: Physical Interconnection
Physical box with backplane
Individual blades plug into backplane slots
Each blade contains one or more network connections

## Slide 3: Logical Interconnection
Known as switching fabric
Handles transport from one blade to another
Becomes bottleneck as number of interfaces scales

## Slide 4: Switching Fabric Properties
Used inside a single network system
Interconnection among I/ O ports (and possibly CPU)
Can transfer unicast, multicast, and broadcast packets
Scales to arbitrary data rate on any port
Scales to arbitrary packet rate on any port
Scales to arbitrary number of ports
Has low overhead
Has low cost

## Slide 5: Types Of Switching Fabrics
Space-division (separate paths)
  Can use multiple paths simultaneously
  Still have port contention
Time-division (shared medium)

## Slide 6: Desires
High speed and low cost!

## Slide 7: Possible Compromise
Separation of physical paths
Less parallel hardware
Crossbar design

## Slide 8: Crossbar
Allows simultaneous transfer on disjoint pairs of ports
Can still have port contention

## Slide 9: Solving Contention
Queues (FIFOs)
  – Attached to input
  – Attached to output
  – At intermediate points

## Slide 10: Time-Division Fabric (shared bus)
Chief advantage: low cost
Chief disadvantage: low speed

## Slide 11: Time-Division Fabric (shared memory)
May be better than shared bus
Usually more expensive

## Slide 12: Multi-Stage Fabrics
Compromise between pure time-division and pure space-division
Attempt to combine advantages of each
  – Lower cost from time-division
  – Higher performance from space-division
Technique: limited sharing

## Slide 13: Banyan Fabric
Example of multi-stage fabric
Features
  – Scalable
  – Self-routing
  – Packet queues allowed, but not required

## Slide 14: Basic Banyan Building Block
Address added to front of each packet
One bit of address used to select output

## Slide 15: Summary
Switching fabric provides connections inside single network system
Two basic approaches
  – Time-division has lowest cost
  – Space-division has highest performance
Multistage designs compromise between two
Banyan fabric is example of multistage