## Slide 1: Network Processor Architectures
Lesson 13

## Slide 2: Architectural Explosion
An excess of exuberance and a lack of experience have produced a wide variety of approaches and architectures.

## Slide 3: Principle Components
Processor hierarchy
Memory hierarchy
Internal transfer mechanisms
External interface and communication mechanisms
Special-purpose hardware
Polling and notification mechanisms
Concurrent and parallel execution support
Programming model and paradigm
Hardware and software dispatch mechanisms

## Slide 4: Processing Hierarchy
Consists of hardware units
Performs various aspects of packet processing
Includes onboard and external processors
Individual processor can be
  – Programmable
  – Configurable
  – Fixed

## Slide 5: Typical Processor Hierarchy
Level Processor Type Programmable? On Chip?
8 General purpose CPU yes possibly
7 Embedded processor yes typically
5 I/O processor yes typically
6 Coprocessor no typically
4 Fabric interface no typically
3 Data transfer unit no typically
2 Framer no possibly
1 Physical transmitter no possibly

## Slide 6: Memory Hierarchy
Memory measurements
  – Random access latency
  – Sequential access latency
  – Throughput
  – Cost
Can be
  – Internal
  – External

## Slide 7: Typical Memory Hierarchy
Memory Type Rel. Speed Approx. Size On Chip?
Control store 100 103 yes
G.P. Registers 90 102 yes
Onboard Cache 40 103 yes
Onboard RAM 7 103 yes
Static RAM 2 107 no
Dynamic RAM 1 108 no

## Slide 8: Internal Transfer Mechanisms
Internal bus
Hardware FIFOs
Transfer registers
Onboard shared memory

## Slide 9: External Interface And Communication Mechanisms
Standard and specialized bus interfaces
Memory interfaces
Direct I/ O interfaces
Switching fabric interface

## Slide 10: Example Interfaces
System Packet Interface Level 3 or 4 (SPI-3 or SPI-4)
SerDes Framer Interface (SFI)
CSIX fabric interface
Note: The Optical Internetworking Forum (OIF) controls the SPI and SFI standards.

## Slide 11: Polling And Notification Mechanisms
Handle asynchronous events
  – Arrival of packet
  – Timer expiration
  – Completion of transfer across the fabric
Two paradigms
  – Polling
  – Notification

## Slide 12: Concurrent Execution Support
Improves overall throughput
Multiple threads of execution
Processor switches context when a thread blocks

## Slide 13: Support For Concurrent Execution
Embedded processor
  – Standard operating system
  – Context switching in software
I/ O processors
  – No operating system
  – Hardware support for context switching
  – Low-overhead or zero-overhead

## Slide 14: Concurrent Support Questions
Local or global threads (does thread execution span multiple processors)?
Forced or voluntary context switching (are threads preemptable)?

## Slide 15: Hardware And Software Dispatch Mechanisms
Refers to overall control of parallel operations
Dispatcher
  – Chooses operation to perform
  – Assigns to a processor

## Slide 16: Implicit And Explicit Parallelism
Explicit parallelism
  – Exposes parallelism to programmer
  – Requires software to understand parallel hardware
Implicit parallelism
  – Hides parallel copies of functional units
  – Software written as if single copy executing

## Slide 17: Architecture Styles, Packet Flow, And Clock Rates
Embedded processor plus fixed coprocessors
Embedded processor plus programmable I/ O processors
Parallel (number of processors scales to handle load)
Pipeline processors
Dataflow

## Slide 18: Embedded Processor Architecture
Single processor
  – Handles all functions
  – Passes packet on
Known as run-to-completion

## Slide 19: Parallel Architecture
Each processor handles 1/N of total load

## Slide 20: Pipeline Architecture
Each processor handles one function
Packet moves through ‘‘pipeline’’

## Slide 21: Clock Rates
Embedded processor runs at > wire speed
Parallel processor runs at < wire speed
Pipeline processor runs at wire speed

## Slide 22: Software Architecture
Central program that invokes coprocessors like subroutines
Central program that interacts with code on intelligent, programmable I/ O processors
Communicating threads
Event-driven program
RPC-style (program partitioned among processors)
Pipeline (even if hardware does not use pipeline)
Combinations of the above

## Slide 23: Example Uses Of Programmable Processors
General purpose CPU
Highest level functionality
Administrative interface
System control
Overall management functions
Routing protocols
Embedded processor
Intermediate functionality
Higher-layer protocols
Control of I/O processors
Exception and error handling
High-level ingress (e.g., reassembly)
High-level egress (e.g., traffic shaping)
I/O processor
Basic packet processing
Classification
Forwarding
Low-level ingress operations
Low-level egress operations

## Slide 24: Using The Processor Hierarchy
To maximize performance, packet processing tasks should be assigned to the lowest level processor capable of performing the task.

## Slide 25: Summary
Network processor architectures characterized by
  – Processor hierarchy
  – Memory hierarchy
  – Internal buses
  – External interfaces
  – Special-purpose functional units
  – Support for concurrent or parallel execution
  – Programming model
  – Dispatch mechanisms