## Slide 1: Intel’s Second Generation Processors
Lesson 26

## Slide 2: Terminology
In the network processor industry, one has to be careful when describing successive versions of network processors because the delay between the announcement of a new product and the actual date at which customers can obtain the product gives a second meaning to the phrase ‘‘later versions of a network processor’’.

## Slide 3: General Characteristics
Same basic architecture
  – Embedded processor
  – Parallel microengines
Enhancements
  – Speed
  – Amount of parallelism
  – Functionality

## Slide 4: Models Of Next Generation Chips
Two primary models
  – Intel® IXP2400 (2.4 Gbps)
  – Intel® IXP2800 (10 Gbps)
Version of 2800 with onboard encryption processor
  – Intel® IXP2850

## Slide 5: Use Of Two Chips For Higher Throughput
Problem
  – One chip insufficient for full duplex
Solution
  – Increase parallelism
  – Use separate chips for ingress and egress processing
Need communication path between them

## Slide 6: Intel® IXP2400 Features
XScale embedded processor (ARM compliant) with caches
Eight microengines (400 or 600 MHz)
Eight hardware threads per microengine
Multiple microengine instruction stores of one thousand
instructions each
Two hundred fifty-six general-purpose registers
Five hundred twelve transfer registers
Addressing for two gigabyte DDR-DRAM
Addressing for thirty-two megabyte QDR-SRAM
Sixteen words of Next Neighbor Registers

## Slide 7: Memory Hierarchy
External DDR-DRAM
External QDR-SRAM
  – Q-array hardware in controller
Onboard Scratchpad memory
Onboard local memory

## Slide 8: External Connections And Buses
No IX bus
High-speed interfaces attach to Media or Switch Fabric (MSF) interface
MSF configurable to
  – Utopia 1, 2, or 3 interface
  – CSIX-L1 fabric interface
  – SPI-3 (POS-PHY 2/3) interface

## Slide 9: Microengine Enhancements
Multiplier unit
Pseudo-random number generator
CRC calculator
Four thirty-two bit timers and timer signaling
Sixteen entry CAM
Timestamping unit
Support for generalized thread signaling
Six hundred forty words of local memory
Queue manipulation mechanism that eliminates the need for mutual exclusion

## Slide 10: Microengine Enhancements (continued)
ATM segmentation and reassembly hardware
Byte alignment facilities
Two ME clusters with independent buses
Called Microengine Version 2

## Slide 11: Other Facilities
Reflector mode pathways
  – Internal, unidirectional buses
  – Allow microengines to communicate
Next Neighbor Registers
  – Pass data from one ME to another
  – Intended for software pipeline

## Slide 12: Intel® IXP2800 Features
Same general architecture as 2400
Sixteen microengines (1.4 GHz)
Two unidirectional sixteen-bit Low Voltage Differential
Signaling data interfaces that can be configured as
  – SPI-4 Phase 2
  – CSIX switching fabric interface
Four QDR-SRAM interfaces (1.6 gigabytes per second
each)
Three RDRAM interfaces (1.6 gigabytes per second each)

## Slide 13: Summary
Intel is moving to second generation of network processors
Three models announced
  – Intel® IXP2400
  – Intel® IXP2800
  – Intel® IXP2850
Same general architecture, except
  – Faster processors
  – More parallelism
  – More hardware facilities
  – Newer, faster external connections