## Slide 1: ACE Run-Time Structure And StrongARM Facilities
Lesson 22

## Slide 2: StrongARM Responsibilities
Loading ACE software
Creating and initializing ACE
Resolving names
Managing the operation of ACEs
Allocating and reclaiming resources (e.g., memory)
Controlling microengine operation
Communication among core components
Interface to non-ACE applications
Interface to operating system facilities
Forwarding packets between core component and microblock(s)

## Slide 3: Components
Object Management System
  – Binds names to objects
  – Contains
    Resolver
    Name server
Resource Manager
  – Access to OS
  – Communication with microengines
  – Memory management

## Slide 4: Components (continued)
Operating System Specific Library
  – Shared library
  – Provides virtual API
  – Should be named OS independent library
Action Services Library
  – Loadable kernel module
  – Run-time support for core component
  – TCP/IP support

## Slide 5: Microengine Assignment
Automated by SDK
Programmer specifies
  – Type (speed) of each port
  – Type of each ACE
SDK chooses
  – Number of replications for each microblock
  – Assignment of microblocks to microengines

## Slide 6: Type Values Used In Configuration File
Only two port types
  – Slow corresponds to 10 / 100 Ethernet
  – Fast corresponds to Gigabit Ethernet
Numeric Value Meaning
0 Slow ingress file
1 Slow egress file
2 Fast ingress file for Port 1
3 Fast ingress file for Port 2
4 Fast egress file

## Slide 7: Pieces Of ACE Code Programmer Writes
Initialization function called when ACE begins
Exception handler receives packets sent by microblock
Action functions that correspond to packet classifications
Crosscalls ACE accepts
Timer functions for timed events
Callback functions for returned values
Termination function called when the ACE terminates

## Slide 8: Reserved Names
SDK software uses fixed names for some functions
Examples
  – ACE initialization function must be named ix_init
  – ACE termination function must be named ix_fini

## Slide 9: Overall Structure Of Core Component
Core component of ACE runs as separate Linux process
Always the same structure
Programmer does not write main program
SDK supplies structure and main program
Uses an event loop

## Slide 10: Conceptual Structure Of ACE Core Component
main( ) /* Core component of an ACE */
{
Intel_init( ); /* Perform internal initialization */
ix_init( ); /* Call user’s initialization function */
Intel_event_loop( ): /* Perform internal event
loop */
ix_fini( ); /* Call user’s termination function */
Intel_fini( ); /* Perform internal cleanup */
exit( ); /* Terminate the Linux process */
}

## Slide 11: Event Loop
Central to asynchronous programming model
Uses polling
Repeatedly checks for presence of event(s) and calls appropriate handler
Can be hidden from programmer
In ACE model
  – Explicit
  – Programmer can modify / extend

## Slide 12: Illustration Of ACE Event Loop
Intel_event_loop( )
{
do forever {
E = getnextevent( );
if (E is termination event) {
return to caller;
} else if (E is exception event) {
call exception handler function;
} else if (E is timer event) {
call timer handler function;
/* Note: additional event tests can be added here*/
}
}
}

## Slide 13: A Note About Event Loops
Beware: although it may seem trivial, the event loop mechanism has several surprising consequences for programmers.

## Slide 14: Event Loop Processing
If event loop stops
  – All processing stops
  – The arrival of a new event will not trigger invocation of an event handler
Conclusion: the event loop must go on

## Slide 15: Asynchronous Programming, Event Loops, Threads, And Blocking
Because each core component executes as a single thread of control, no handler function is permitted to block because doing so will stop the event loop and block the entire core component

## Slide 16: Prohibition On Blocking Calls
Programmer must use asynchronous call model
Calling program specifies
  – Function to invoke
  – Arguments to pass
  – Callback function
Called program
  – Invoked asynchronously
  – Receives copy of arguments, and computes result
  – Specifies callback to be invoked

## Slide 17: Illustration Of Asynchronous Callback (part 1)
h { /* Synchronous version */
y = f ( x ); /* Call f (potentially blocking) */
z = g( y ); /* Use the result from f to call g */
q += z; /* Use the value of z to update q*/
return;
}
h1 { /* Asynchronous version */
allocate global variables y, z, and q;
establish cbf1 as the callback function for f1;
establish cbg1 as the callback function for g1;
Start f1(x) with a nonblocking call;
return;
}

## Slide 18: Illustration Of Asynchronous Callback (part 2)
function cbf1(retval) { /* Callback function for f1 */
y = retval;
start g1(y) with a nonblocking call;
return;
}
function cbg1(retval) { /* Callback function for g1 */
z = retval;
q += z;
return;
}

## Slide 19: Code Complexity
Because it uses the asynchronous paradigm, the core component of an ACE is usually significantly more complex and difficult to understand than a synchronous program that solves the same problem.

## Slide 20: Some Good News
ACE core component structured around event loop
Underlying system is sequential
No mutual exclusion needed!

## Slide 21: Some Good News
ACE core component structured around event loop
Underlying system is sequential
No mutual exclusion needed!

## Slide 22: Memory Allocation
Performed by StrongARM
Function RmMalloc (in Resource Manager) allocates memory
Request must specify type of memory
  – SRAM
  – SDRAM
  – Scratch
Function RmGetPhysOffset maps virtual address to physical address
Resulting physical address passed to microblock

## Slide 23: Steps Taken At System Startup
Load and start ASL kernel module, name server, and resolver
Load and start device drivers for the network interfaces
Load and initialize the Resource Manager which determines how many copies of each ingress and egress microblock group to run
Parse and check configuration file ixsys.config
Start core component of each ACE, which causes ACE to invoke ix_init function

## Slide 24: Steps Taken At System Startup (continued)
Turn on interfaces, assign microblock groups to microengines, and resolve external references (known as patching)
Bind the ACE targets and physical interfaces
Start microengines running

## Slide 25: ACE Data Structure
Stores information needed by Intel® SDK software
Must be allocated by ix_init and deallocated by ix_fini
Uses structure ix_ace
Can be extended with data defined by programmer

## Slide 26: Example ACE Data Declaration
#include <ix/asl.h> /* Include Intel’s library declarations*/
structmyace { /* Programmer’s control block */
struct ix_ace ace; /* Intel’s ace embedded as first item*/
int mycount; /* Counter used by programmer’s code*/
/* Programmer can insert additional data items here... */
}

## Slide 27: Example Data Structure Allocation
ix_init ( ... , ix_ace **app , ... )
{
struct myace *ap; /* Ptr to programmer’s control block*/
ap = malloc ( sizeof ( struct myace ) ) ;
*app = &ap->ace ;
ix_ace_init ( &ap->ace ) ;
/* Other initialization code goes here... */
}

## Slide 28: Crosscall
Uses OMS
Three types
  – Oneway: no return
  – Twoway: conventional procedure call
  – Deferred: asynchronous return through callback

## Slide 29: Possible Crosscall Communication
Caller Called Procedure Block?
ACE core component ACE core component no
ACE core component non-ACE application no
non-ACE application ACE core component no
non-ACE application non-ACE application yes

## Slide 30: Crosscall Declaration
Uses Interface Definition Language (IDL)
Declares type of
  – Exported function
  – Arguments

## Slide 31: Example IDL Declaration
interface PacketCounter
{
struct packetinfo {
int numpackets; /* Count of total packets */
int numbcasts; /* Count of broadcast packets*/
};
oneway void incTcount ( in int addedpackets ) ;
deferred int resetTcount ( in int newnumpkts ) ;
twoway int resetPinfo ( in struct packetinfo ) ;
};

## Slide 32: Timer Management
Performed on StrongARM
Uses OMS
Follows asynchronous model

## Slide 33: Using A Timer
Initialize H, a handle for an ix_event.
Associate handle H with a callback function, CB.
Calculate T, a time for the event to occur.
Schedule event H at time T.
At any time prior to T, event H can be cancelled.
At time T, function CB will be called if the event has not been cancelled.

## Slide 34: Summary
Core component of ACE
  – Runs as Linux process
  – Provides asynchronous API
  – Uses event loop mechanism
  – Includes functions named ix_init and ix_fini
  – Responsible for memory allocation and timer management