## Slide 1: Packet Processor Hardware (Microengines And FBI)
Lesson 19

## Slide 2: Role Of Microengines
Packet ingress from physical layer hardware
Checksum verification
Header processing and classification
Packet buffering in memory
Table lookup and forwarding
Header modification
Checksum computation
Packet egress to physical layer hardware

## Slide 3: Microengine Characteristics
Programmable microcontroller
RISC design
One hundred twenty-eight general-purpose registers
One hundred twenty-eight transfer registers
Hardware support for four threads and context switching
Five-stage execution pipeline
Control of an Arithmetic Logic Unit (ALU)
Direct access to various functional units

## Slide 4: Microengine Level
Not a typical CPU
Does not contain native instruction for each operation
Really a microsequencer

## Slide 5: Consequence Of Microsequencing
Because it functions as a microsequencer, a microengine does not provide native hardware instructions for arithmetic operations, nor does it provide addressing modes for direct memory access. Instead, a program running on a microengine controls and uses functional units on the chip to access memory and perform operations.

## Slide 6: Microengine Instruction Set

## Slide 7: Microengine View Of Memory
Separate address spaces
Specific instruction to reference each memory type
  – Instruction sdram to access SDRAM memory
  – Instruction sram to access SRAM memory
  – Instruction scratch to access Scratchpad memory
Consequence: early binding of data to memory

## Slide 8: Five-Stage Instruction Pipeline
Stage Description
Fetch the next instruction
Decode the instruction and get register address(es)
Extract the operands from registers
Perform ALU, shift, or compare operations and set the condition codes
Write the results to the destination register

## Slide 9: Instruction Stall
Occurs when operand not available
Processor temporarily stops execution
Reduces overall speed
Should be avoided when possible

## Slide 10: Example Instruction Stall
Consider two instructions:
K: ALU operation to add the contents of R1 to R2
K+1: ALU operation to add the contents of R2 to R3
Second instruction cannot access R2 until value has been written
Stall occurs

## Slide 11: Sources Of Delay
Access to result of previous / earlier operation
Conditional branch
Memory access

## Slide 12: Memory Access Delays
Type Of Approximate Access Time
Memory (in clock cycles)
Scratchpad 12 - 14
SRAM 16 - 20
SDRAM 32 - 40
Delay is surprisingly large

## Slide 13: Threads Of Execution
Technique used to speed processing
Multiple threads of execution remain ready to run
Program defines threads and informs processor
Processor runs one thread at a time
Processor automatically switches context to another thread when current thread blocks
Known as hardware threads

## Slide 14: The Point Of Hardware Threads
Hardware threads increase overall throughput by allowing a microengine to handle up to four packets concurrently; with threads, computation can proceed without waiting for memory access.

## Slide 15: .Context Switching Time
Low-overhead context switch means one instruction delay as hardware switches from one thread to another
Zero-overhead context switch means no delay during context switch
Intel® IXP1200 offers zero-overhead context switch

## Slide 16: Microengine Instruction Store
Private instruction store per microengine
Advantage: no contention
Disadvantage: small (1024 instructions)

## Slide 17: General-Purpose Registers
One hundred twenty-eight per microengine
Thirty-two bits each
Used for computation or intermediate values
Divided into banks
Context-relative or absolute addresses

## Slide 18: Forms Of Addressing
Absolute
  – Entire set available
  – Uses integer from 0 to 127
Context-relative
  – One quarter of set available to each thread
  – Uses integer from 0 to 31
  – Allows same code to run on multiple microengines

## Slide 19: Register Banks
Mechanism commonly used with RISC processor
Registers divided into A bank and B bank
Maximum performance achieved when each instruction references a register from the A bank and a register from the B bank

## Slide 20: Transfer Registers
Used to buffer external memory transfers
Example: read a value from memory
  – Copy value from memory into transfer register
  – Move value from transfer register into general-purpose register
One hundred twenty-eight per microengine
Divided into four types
  – SRAM or SDRAM
  – Read or write

## Slide 21: Local Control And Status Registers
Used to interrogate or control the Intel® IXP1200
All mapped into StrongARM address space
Microengine can only access its own local CSRs

## Slide 22: Local CSRs
Local CSR Purpose
USTORE_ADDRESS Load the microengine control store
USTORE_DATA Load a value into the control store
ALU_OUTPUT Debugging: allows StrongARM to read
GPRs and transfer registers
ACTIVE_CTX_STS Determine context status
ENABLE_SRAM_JOURNALING Debugging: place journal in SRAM
CTX_ARB_CTL Context arbiter control
CTX_ENABLES Debugging: enable a context
CC_ENABLE Enable condition codes
CTX_n_STS Determine context status
CTX_n_SIG_EVENTS Determine signal status
CTX_n_WAKEUP_EVENTS Determine which wakeup events
are currently enabled
Note: n is digit from 0 through 3 (hardware contains a separate
CSR for each of the four contexts).

## Slide 23: Interprocessor Communication Mechanisms
Thread-to-StrongARM communication
  – Interrupt
  – Signal event
Thread-to-thread communication within one Intel® IXP1200
  – Signal event
Thread-to-thread communication across multiple Intel® IXP1200s
  – Ready bus

## Slide 24: FBI Unit
Interface between processors and other functional units
  – Scratchpad memory
  – Hash unit
  – FBI control and status registers
  – Control and operation of the Ready bus
  – Control and operation of the IX bus
  – Data buffers that hold data arriving from the IX bus
  – Data buffers that hold data sent to the IX bus
Operates like DMA controller
Uses FIFOs

## Slide 25: FIFOs
Hardware buffers
Transfer performed in 64 byte blocks
Misleading name: access is random
Only path between external device and microengine
Receive FIFO (RFIFO)
  – Handles input
  – Physical interface moves data to RFIFO
  – FBI moves data from RFIFO to memory

## Slide 26: FIFOs (continued)
Transmit FIFO (TFIFO)
  – Handles output
  – FBI moves data from memory to TFIFO
  – Physical interface extracts data from TFIFO

## Slide 27: A Note About FIFO Transfer
It is possible for a microengine to transfer data to or from a FIFO without going to memory.

## Slide 28: FBI
Initiates and controls data transfer
Contains active components
  – Push engine
  – Pull engine

## Slide 29: ScratchPad Memory
Organized into 1K words of 4 bytes each
Offers special facilities
  – Test-and-set of individual bits
  – Autoincrement (low latency)

## Slide 30: Hash Unit
Configurable coprocessor
Operates asynchronously
Intended for table lookup when multiplication or division
required (ALU does not have multiply instruction)

## Slide 31: Hash Unit Computation
Computes quotient Q(x) and remainder R(x):
A(x) * M(x) / G(x) ® Q(x) + R(x)
A(x) is input value
M(x) is hash multiplier (configurable)
G(x) is built-in value
Two values for G — one for 48-bit hash, one for 64-bit hash

## Slide 32: Hash Mathematics
Integer value interpreted as polynomial over field [0,1]
Example:
2040116
Is interpreted as
x17 + x10 + 1
Similarly, value G(x) used in 48-bit hash
100100200040116
Is interpreted as
x48 + x36 + x25 + x10 + 1

## Slide 33: Hash Example
A = 80000000000116 ( x47 + 1 )
G = 100100200040116 ( x48 + x36 + x 25 + x 10 + 1 )
M = 20D16 ( x9 + x3 + x2 + 1 )
Hash computes R, remainder of M times A divided by G
H(X) = R = M * A % G

## Slide 34: Hash Example (continued)
Multiplying yields
M * A = x56 + x50 + x49 + x47 + x9 + x3 + x2 + 1
Furthermore
M * A = Q * G + R
Where
Q = x8 + x2 + x1

## Slide 35: Hash Example (continued)
So, Q is:
10616
And R is:
x47 + x44 + x38 + x37 + x33 + x27 + x26 + x18 + x12 +
x11 + x9 + x8 + x3 + x1 + 1
The hash unit returns R as the value of the computation:
90620C041B0B16

## Slide 36: Other Intel® IXP1200 Hardware
The Intel® IXP1200 contains over 1500 registers used for
  Configuration and bootstrapping
  – Control of functional units and buses
  – Checking status of processors, threads, and onboard functional units
Example: IX bus registers used to
  – Control bus operation
  – Configure the bus for 64-bit or 32-bit mode operation
  – Control devices attached to the bus
  Specify whether a MAC device or the Intel® IXP handles control signals

## Slide 37: Summary
Microengines
  – Low-level, programmable packet processors
  – Use RISC design with instruction pipeline
  – Have hardware threads for higher throughput
  – Use transfer registers to access memory
  – Use FIFOs for I/ O
  – Do not have multiply, but have access to hash unit