## Slide 1: The Complexity Of Network Processor Design
Lesson 12

## Slide 2: How Should A Network Processor Be Designed?
Depends on
  – Operations network processor will perform
  – Role of network processor in overall system

## Slide 3: Goals
Generality
  – Sufficient for all protocols
  – Sufficient for all protocol processing tasks
  – Sufficient for all possible networks
High speed
  – Scale to high bit rates
  – Scale to high packet rates
Elegance
  – Minimality, not merely comprehensiveness

## Slide 4: The Key Point
A network processor is not designed to process a specific protocol or part of a protocol. Instead, designers seek a minimal set of instructions that are sufficient to handle an arbitrary protocol processing task at high speed.

## Slide 5: Network Processor Design
To understand network processors, consider problem to be solved
  – Protocols being implemented
  – Packet processing tasks

## Slide 6: Packet Processing Functions
Error detection and correction
Traffic measurement and policing
Frame and protocol demultiplexing
Address lookup and packet forwarding
Segmentation, fragmentation, and reassembly
Packet classification
Traffic shaping
Timing and scheduling
Queueing
Security: authentication and privacy

## Slide 7: Questions
Does our list of functions encompass all protocol processing?
Which function(s) are most important to optimize?
How do the functions map onto hardware units in a typical network system?
Which hardware units in a network system can be replaced with network processors?
What minimal set of instructions is sufficiently general to implement all functions?

## Slide 8: Division Of Functionality
Partition problem to reduce complexity
Basic division into two parts
Functions applied when packet arrives known as ingress processing
Functions applied when packet leaves known as egress processing

## Slide 9: Ingress Processing
Security and error detection
Classification or demultiplexing
Traffic measurement and policing
Address lookup and packet forwarding
Header modification and transport splicing
Reassembly or flow termination
Forwarding, queueing, and scheduling

## Slide 10: Egress Processing
Addition of error detection codes
Address lookup and packet forwarding
Segmentation or fragmentation
Traffic shaping
Timing and scheduling
Queueing and buffering
Output security processing

## Slide 11: A Note About Scalability
Unlike a conventional processor, scalability is essential for network processors. To achieve maximum scalability, a network processor offers a variety of special-purpose functional units, allows parallel or pipelined execution, and operates in a distributed environment.

## Slide 12: How Will Network Processors Be Used?
For ingress processing only?
For egress processing only?
For combination?

## Slide 13: How Will Network Processors Be Used?
For ingress processing only?
For egress processing only?
For combination?
Answer: No single role

## Slide 14: Potential Architectural Roles For Network Processor
Replacement for a conventional CPU
Augmentation of a conventional CPU
On the input path of a network interface card
Between a network interface card and central interconnect
Between central interconnect and an output interface
On the output path of a network interface card
Attached to central interconnect like other ports

## Slide 15: An Interesting Potential Role For Network Processors
In addition to replacing elements of a traditional third generation architecture, network processors can be attached directly to a central interconnect and used to implement stages of a macroscopic data pipeline. The interconnect allows forwarding among stages to be optimized.

## Slide 16: Conventional Processor Design
Design an instruction set, S
Build an emulator/ simulator for S in software
Build a compiler that translates into S
Compile and emulate example programs
Compare results to
  – Extant processors
  – Alternative designs

## Slide 17: Network Processor Emulation
Can emulate low-level logic (e.g., Verilog)
Software implementation
  – Slow
  – Cannot handle real packet traffic
FPGA implementation
  – Expensive and time-consuming
  – Difficult to make major changes

## Slide 18: Network Processor Design
Unlike conventional processor design
No existing code base
No prior hardware experience
Each design differs

## Slide 19: Hardware And Software Design
Because a network processor includes many low-level hardware details that require specialized software, the hardware and software designs are codependent; software for a network processor must be created along with the hardware.

## Slide 20: Summary
Protocol processing divided into ingress and egress operations
Network processor design is challenging because
  – Desire generality and efficiency
  – No existing code base
  – Software designs evolving with hardware