## Slide 1: Programming Model (Intel® ACE)
Lesson 21

## Slide 2: Active Computing Element (ACE)
Defined by Intel’s SDK
Not part of hardware

## Slide 3: ACE Features
Fundamental software building block
Used to construct packet processing systems
Runs on StrongARM, microengine, or host
Handles control plane and fast or slow data path processing
Coordinates and synchronizes with other ACEs
Can have multiple inputs or outputs
Can serve as part of a pipeline

## Slide 4: ACE Terminology
Library ACE
  – Built by Intel
  – Available with SDK
Conventional ACE
  – Built by Intel customers
  – Can incorporate items from Action Service Libraries
MicroACE
  – Core component runs on StrongARM
  – Microblock component runs on microengine

## Slide 5: More Terminology
Source microblock
  – Handles ingress from I/ O device
Sink microblock
  – Handles egress to I/ O device
Transform microblock
  – Intermediate position in a pipeline

## Slide 6: Four Conceptual Parts Of An ACE
Initialization
Classification
Actions associated with each classification
Message and event management

## Slide 7: Output Targets And Late Binding
ACE has set of outputs
Each output given target name
Outputs bound dynamically at run time
Unbound target corresponds to packet discard

## Slide 8: Conceptual ACE Interconnection
Ingress ACE acts as source
Process ACE acts as transform
Egress ACE acts as sink
Connections created at run time
Ingress Ace
Process Ace
Egress Ace
Input
ports
Output
ports

## Slide 9: Components Of MicroACE (review)
Single ACE with two components
  – StrongARM (core component)
  – Microengines (microblock component)
Communication possible between components

## Slide 10: Division Of ACE Into Components
Microblocks form fast path
Stack ACE runs entirely on StrongARM

## Slide 11: Microblock Group
Set of one or more microblocks
Treated as single unit
Loaded onto microengine for execution
Can be replicated on multiple microengines for higher speed

## Slide 12: Replication Of Microblock Group
Typically used for
  – Ingress microblock group
  – Egress microblock group
Replications depend on number and speed of interfaces
SDK software computes replications automatically

## Slide 13: Microblock Structure
Asynchronous model
Programmer creates
  – Initialization macro
  – Dispatch loop

## Slide 14: Dispatch Loop
Determines disposition of each packet
Uses return code to either
  – Send packet to StrongARM
  – Forward packet to ‘‘next’’ microblock
  – Discard packet

## Slide 15: Dispatch Loop Algorithm
Allocate global registers;
Initialize dispatch loop; Initialize Ethernet devices;
Initialize ingress microblock; Initialize IP microblock;
while (1) {
Get next packet from input device(s);
Invoke ingress microblock;
if ( return code == 0 ) {
Drop the packet;
} else if ( return code == 1 ) {
Send packet to ingress core component;
} else { /* IP packet */
Invoke IP microblock;
if ( return code == 0 ) {
Drop packet;
} else if ( return code == 1 ) {
Send packet to IP core component;
} else {
Send packet to egress microblock;
}
}
}

## Slide 16: Arguments Passed To Processing Macro
A buffer handle for a frame that contains a packet
A set of state registers
  – Contain information about the frame
  – Can be modified
A variable named dl_next_block
  – Used to store return code

## Slide 17: Packet Queues
Placed between ACE components
Buffer packets
Permit asynchronous operation

## Slide 18: Exceptions
Packets passed from microblock to core component
Mechanism
  – Microcode sets dl_next_block to IX_EXCEPTION
  – Dispatch loop forwards packet to core
  – ACE tag used to identify corresponding component
  – Exception handler is invoked in core component

## Slide 19: Possible Actions Core Component Applies To Exception
Consume the packet and free the buffer
Modify the packet before sending it on
Send the packet back to the microblock for further processing
Forward the packet to another ACE on the StrongARM

## Slide 20: Crosscall Mechanism
Used between
  – Core component of one ACE and another
  – ACE core component and non-ACE application
Not intended for packet transfer
Operates like Remote Procedure Call (RPC)
Mechanism known as crosscall

## Slide 21: Crosscall Implementation
Both caller and callee programmed to use crosscall
Declaration given in Interface Definition Language (IDL)
IDL compiler
  – Reads specification
  – Generates stubs that handle calling details

## Slide 22: Crosscall Implementation (continued)
Three types of crosscalls
  – Deferred: caller does not block; return notification asynchronous
  – Oneway: caller does not block; no value returned
  – Twoway: caller blocks; callee returns a value
Twoway call corresponds to traditional RPC
Type of call determined at compile time

## Slide 23: Twoway Calling And Blocking
Because the core component of an ACE is prohibited from blocking, an ACE cannot make a twoway call.

## Slide 24: Summary
Intel® SDK uses ACE programming model
ACE
  – Basic unit of computation
  – Can include code for StrongARM (core) and microengines (microblock)
Packet queues used to pass packets between ACEs
Crosscall mechanism used for nonpacket communication