## Slide 1: Hardware Architectures For Protocol Processing And Aggregate Rates
Lesson 8

## Slide 2: A Brief History Of Computer Hardware
1940s
  – Beginnings
1950s
  Consolidation on von Neumann architecture
  – I/ O controlled by CPU
1960s
  – I/ O becomes important
  – Evolution of third generation architecture with interrupts

## Slide 3: I/ O Processing
Evolved from after-thought to central influence
Low-end systems (e.g., microcontrollers)
  – Dumb I/ O interfaces
  – CPU does all the work (polls devices)
  – Single, shared memory
  – Low cost, but low speed

## Slide 4: I/ O Processing (continued)
Mid-range systems (e.g., minicomputers)
  – Single, shared memory
  – I/ O interfaces contain logic for transfer and status operations
  – CPU
    Starts device then resumes processing
  – Device
    Transfers data to / from memory
    Interrupts when operation complete

## Slide 5: I/ O Processing (continued)
High-end systems (e.g., mainframes)
  – Separate, programmable I/ O processor
  – OS downloads code to be run
  – Device has private on-board buffer memory
  – Examples: IBM channel, CDC peripheral processor

## Slide 6: Networking Systems Evolution
Twenty year history
Same trend as computer architecture
  – Began with central CPU
  – Shift to emphasis on I/ O
Three main generations

## Slide 7: First Generation Network Systems
Traditional software-based router
Used conventional (minicomputer) hardware
  – Single general-purpose processor
  – Single shared memory
  – I/ O over a bus
  – Network interface cards use same design as other I/ O devices

## Slide 8: Protocol Processing In First Generation Network Systems
General-purpose processor handles most tasks
Sufficient for low-speed systems
Note: we will examine other generations later in the course

## Slide 9: How Fast Does A CPU Need To Be?
Depends on
  – Rate at which data arrives
  – Amount of processing to be performed

## Slide 10: Two Measures Of Speed
Data rate (bits per second)
  – Per interface rate
  – Aggregate rate
Packet rate (packets per second)
  – Per interface rate
  – Aggregate rate

## Slide 11: How Fast Is A Fast Connection?
Definition of fast data rate keeps changing
  – 1960: 10 Kbps
  – 1970: 1 Mbps
  – 1980: 10 Mbps
  – 1990: 100 Mbps
  – 2000: 1000 Mbps (1 Gbps)
  – 2003: 2400 Mbps

## Slide 12: How Fast Is A Fast Connection?
Definition of fast data rate keeps changing
  – 1960: 10 Kbps
  – 1970: 1 Mbps
  – 1980: 10 Mbps
  – 1990: 100 Mbps
  – 2000: 1000 Mbps (1 Gbps)
  – 2003: 2400 Mbps
  – Soon: 10 Gbps???

## Slide 13: Aggregate Rate Vs. Per-Interface Rate
Interface rate
  – Rate at which data enters / leaves
Aggregate
  – Sum of interface rates
  – Measure of total data rate system can handle
Note: aggregate rate crucial if CPU handles traffic from all interfaces

## Slide 14: A Note About System Scale
The aggregate data rate is defined to be the sum of the rates at which traffic enters or leaves a system. The maximum aggregate data rate of a system is important because it limits the type and number of network connections the system can handle.

## Slide 15: Packet Rate Vs. Data Rate
Sources of CPU overhead
  – Per-bit processing
  – Per-packet processing
Interface hardware handles much of per-bit processing

## Slide 16: A Note About System Scale
For protocol processing tasks that have a fixed cost per packet, the number of packets processed is more important than the aggregate data rate.

## Slide 17: Example Packet Rates
Technology Network Packet Rate Packet Rate
Data Rate For Small Packets For Large Packets
In Gbps In Kpps In Kpps
10Base-T 0.010 19.5 0.8
100Base-T 0.100 195.3 8.2
OC-3 0.156 303.8 12.8
OC-12 0.622 1,214.8 51.2
1000Base-T 1.000 1,953.1 82.3
OC-48 2.488 4,860.0 204.9
OC-192 9.953 19,440.0 819.6
OC-768 39.813 77,760.0 3,278.4
Key concept: maximum packet rate occurs with minimum-size packets

## Slide 18: Time Per Packet
Technology Time per packet Time per packet
for small packets for large packets
( in µs ) ( in µs )
10Base-T 51.20 1,214.40
100Base-T 5.12 121.44
OC-3 3.29 78.09
OC-12 0.82 19.52
1000Base-T 0.51 12.14
OC-48 0.21 4.88
OC-192 0.05 1.22
OC-768 0.01 0.31
Note: these numbers are for a single connection!

## Slide 19: Conclusion
Software running on a general-purpose processor is an insufficient architecture to handle high-speed networks because the aggregate packet rate exceeds the capabilities of a CPU.

## Slide 20: Possible Ways To Solve The CPU Bottleneck
Fine-grain parallelism
Symmetric coarse-grain parallelism
Asymmetric coarse-grain parallelism
Special-purpose coprocessors
NICs with onboard processing
Smart NICs with onboard stacks
Cell switching
Data pipelines

## Slide 21: Fine-Grain Parallelism
Multiple processors
Instruction-level parallelism
Example:
  – Parallel checksum: add values of eight consecutive memory locations at the same time
Assessment: insignificant advantages for packet processing

## Slide 22: Symmetric Coarse-Grain Parallelism
Symmetric multiprocessor hardware
  – Multiple, identical processors
Typical design: each CPU operates on one packet
Requires coordination
Assessment: coordination and data access means N
processors cannot handle N times more packets than one processor

## Slide 23: Asymmetric Coarse-Grain Parallelism
Multiple processors
Each processor
  – Optimized for specific task
  – Includes generic instructions for control
Assessment
  – Same problems of coordination and data access as symmetric case
  – Designer much choose how many copies of each processor type

## Slide 24: Special-Purpose Coprocessors
Special-purpose hardware
Added to conventional processor to speed computation
Invoked like software subroutine
Typical implementation: ASIC chip
Choose operations that yield greatest improvement in speed

## Slide 25: General Principle
To optimize computation, move operations that account for the most CPU time from software into hardware.

## Slide 26: General Principle
To optimize computation, move operations that account for the most CPU time from software into hardware.
Idea known as Amdahl’s law (performance improvement from faster hardware technology is limited to the fraction of time the faster technology can be used)

## Slide 27: NICs And Onboard Processing
Basic optimizations
  – Onboard address recognition and filtering
  – Onboard buffering
  – DMA
  – Buffer and operation chaining
Further optimization possible

## Slide 28: Smart NICs With Onboard Stacks
Add hardware to NIC
  – Off-the-shelf chips for layer 2
  – ASICs for layer 3
Allows each NIC to operate independently
  – Effectively a multiprocessor
  – Total processing power increased dramatically

## Slide 29: Smart NICs With Onboard Processing
NIC handles layers 2 and 3
CPU only handles exceptions

## Slide 30: Cell Switching
Alternative to new hardware
Changes
  – Basic paradigm
  – All details (e.g., protocols)
Connection-oriented

## Slide 31: Cell Switching Details
Fixed-size packets
  – Allows fixed-size buffers
  – Guaranteed time to transmit/ receive
Relative (connection-oriented) addressing
  – Smaller address size
  – Label on packet changes at each switch
  – Requires connection setup
Example: ATM

## Slide 32: Data Pipeline
Move each packet through series of processors
Each processor handles some tasks
Assessment
  – Well-suited to many protocol processing tasks
  – Individual processor can be fast

## Slide 33: Summary
Packet rate can be more important than data rate
Highest packet rate achieved with smallest packets
Rates measured per interface or aggregate
Special hardware needed for highest-speed network systems
  – Smart NIC can include part of protocol stack
  – Parallel and pipelined hardware also possible