## Slide 1: Basic Packet Processing: Algorithms And Data Structures
Lesson 5

## Slide 2: Copying
Used when packet moved from one memory location to another
Expensive
Must be avoided whenever possible
– Leave packet in buffer
– Pass buffer address among threads/layers

## Slide 3: Buffer Allocation
Possibilities
  – Large, fixed buffers
  – Variable-size buffers
  – Linked list of fixed-size blocks

## Slide 4: Buffer Addressing
Buffer address must be resolvable in all contexts
Easiest implementation: keep buffers in kernel space

## Slide 5: Integer Representation
Two standards
  – Little endian (least-significant byte at lowest address)
  – Big endian (most-significant byte at lowest address)

## Slide 6: Integer Conversion
Needed when heterogeneous computers communicate
Protocols define network byte order
Computers convert to network byte order
Typical library functions
  Function data size Translation
  ntohs 16 bits Network byte order to host’s byte order
  htons 16 bits Host’s byte order to network byte order
  ntohl 32 bits Network byte order to host’s byte order
  htonl 32 bits Host’s byte order to network byte order

## Slide 7: Examples Of Algorithms Implemented With Software-Based Systems
Layer 2
  Ethernet bridge
Layer 3
  IP forwarding
  IP fragmentation and reassembly
Layer 4
  – TCP connection recognition and splicing
Other
  – Hash table lookup

## Slide 8: Why Study These Algorithms?
Provide insight on packet processing tasks
Reinforce concepts
Help students recall protocol details
You will need them in lab!

## Slide 9: Ethernet Bridge
Used between a pair of Ethernets
Provides transparent connection
Listens in promiscuous mode
Forwards frames in both directions
Uses addresses to filter

## Slide 10: Bridge Filtering
Uses source address in frames to identify computers on each network
Uses destination address to decide whether to forward frame

## Slide 11: Bridge Algorithm
Assume: two network interfaces each operating in promiscuous mode.
Create an empty list, L, that will contain pairs of values;
Do forever {
Acquire the next frame to arrive;
Set I to the interface over which the frame arrived;
Extract the source address, S;
Extract the destination address, D;
Add the pair ( S, I ) to list L if not already present.
If the pair ( D, I ) appears in list L {
Drop the frame;
} Else {
Forward the frame over the other interface;
}
}

## Slide 12: Implementation Of Table Lookup
Need high speed (more on this later)
Software-based systems typically use hashing for table lookup

## Slide 13: Hashing
Optimizes number of probes
Works well if table not full
Practical technique: double hashing

## Slide 14: Hashing Algorithm
Given: a key, a table in memory, and the table size N.
Produce: a slot in the table that corresponds to the key
or an empty table slot if the key is not in the table.
Method: double hashing with open addressing.
Choose P1 and P2 to be prime numbers;
Fold the key to produce an integer, K;
Compute table pointer Q equal to (P1 x K ) modulo N;
Compute increment R equal to (P2 x K ) modulo N;
While (table slot Q not equal to K and nonempty) {
Q (Q + R) modulo N;
}
At this point, Q either points to an empty table slot or to the
slot containing the key.

## Slide 15: Address Lookup
Computer can compare integer in one operation
Network address can be longer than integer (e.g., 48 bits)
Two possibilities
  –Use multiple comparisons per probe
  – Fold address into integer key

## Slide 16: Folding
Maps N-bit value into M-bit key, M < N
Typical technique: exclusive or
Potential problem: two values map to same key
Solution: compare full value when key matches

## Slide 17: IP Forwarding
Used in hosts as well as routers
Conceptual mapping
(next hop, interface) f (datagram, routing table)
Table driven

## Slide 18: IP Routing Table
One entry per destination
Entry contains
– 32-bit IP address of destination
  – 32-bit address mask
  – 32-bit next-hop address
  – N-bit interface number

## Slide 19: Example IP Routing Table
Destination Address Next-Hop Interface
Address Mask Address Number
192.5.48.0 255.255.255.0 128.210.30.5 2
128.10.0.0 255.255.0.0 128.210.141.12 1
0.0.0.0 0.0.0.0 128.210.30.5 2
Values stored in binary
Interface number is for internal use only
Zero mask produces default route

## Slide 20: IP Forwarding Algorithm
Given: destination address A and routing table R.
Find: a next hop and interface used to route datagrams to A.
For each entry in table R {
Set MASK to the Address Mask in the entry;
Set DEST to the Destination Address in the entry;
If (A & MASK) == DEST {
Stop; use the next hop and interface in the entry;
}
}
If this point is reached, declare error: no route exists;

## Slide 21: IP Fragmentation
Needed when datagram larger than network MTU
Divides IP datagram into fragments
Uses FLAGS bits in datagram header
NEED to show FLAGS bits

## Slide 22: IP Fragmentation Algorithm (Part 1: Initialization)
Given: an IP datagram, D, and a network MTU.
Produce: a set of fragments for D.
If the DO NOT FRAGMENT bit is set {
Stop and report an error;
}
Compute the size of the datagram header, H;
Choose N to be the largest multiple of 8 such
That H+N ≤ MTU;
Initialize an offset counter, O, to zero;

## Slide 23: IP Fragmentation Algorithm (Part 2: Processing)
Repeat until datagram empty {
Create a new fragment that has a copy of D’s header;
Extract up to the next N octets of data from D and place
the data in the fragment;
Set the MORE FRAGMENTS bit in fragment header;
Set TOTAL LENGTH field in fragment header to be H+N;
Set FRAGMENT OFFSET field in fragment header to O;
Compute and set the CHECKSUM field in fragment
header;
Increment O by N/ 8;
}

## Slide 24: Reassembly
Complement of fragmentation
Uses IP SOURCE ADDRESS and IDENTIFICATION fields in datagram header to group related fragments
Joins fragments to form original datagram

## Slide 25: Reassembly Algorithm
Given: a fragment, F, add to a partial reassembly.
Method: maintain a set of fragments for each datagram.
Extract the IP source address, S, and ID fields from F;
Combine S and ID to produce a lookup key, K;
Find the fragment set with key K or create a new set;
Insert F into the set;
If the set contains all the data for the datagram {
Form a completely reassembled datagram and process it;
}

## Slide 26: Data Structure For Reassembly
Two parts
  Buffer large enough to hold original datagram
  Linked list of pieces that have arrived

## Slide 27: TCP Connection
Involves a pair of endpoints
Started with SYN segment
Terminated with FIN or RESET segment
Identified by 4-tuple
( src addr, dest addr, src port, dest port )

## Slide 28: TCP Connection Recognition Algorithm (Part 1)
Given: a copy of traffic passing across a network.
Produce: a record of TCP connections present in the traffic.
Initialize a connection table, C, to empty;
For each IP datagram that carries a TCP segment {
Extract the IP source, S, and destination, D, addresses;
Extract the source, P 1 , and destination, P 2 , port numbers;
Use (S,D,P 1 , P 2 ) as a lookup key for table C and
create a new entry, if needed;

## Slide 29: TCP Connection Recognition Algorithm (Part 2)
If the segment has the RESET bit set, delete the entry;
Else if the segment has the FIN bit set, mark the
connection
closed in one direction, removing the entry from C if
the connection was previously closed in the other;
Else if the segment has the SYN bit set, mark the
connection as
being established in one direction, making it completely established if it was previously marked as being established in the other;
}

## Slide 30: TCP Splicing
Join two TCP connections
Allow data to pass between them
To avoid termination overhead translate segment header fields
  – Acknowledgement number
  – Sequence number

## Slide 31: TCP Splicing Algorithm (Part 1)
Given: two TCP connections.
Produce: sequence translations for splicing the connection.
Compute D1, the difference between the starting sequences on incoming connection 1 and outgoing connection 2;
Compute D2, the difference between the starting sequences on incoming connection 2 and outgoing connection 1;

## Slide 32: TCP Splicing Algorithm (Part 2)
For each segment {
If segment arrived on connection 1 {
Add D1 to sequence number;
Subtract D2 from acknowledgement number;
} else if segment arrived on connection 2 {
Add D2 to sequence number;
Subtract D1 from acknowledgement number;
}
}

## Slide 33: Summary
Packet processing algorithms include
  – Ethernet bridging
  – IP fragmentation and reassembly
  – IP forwarding
  – TCP splicing
Table lookup important
  – Full match for layer 2
  – Longest prefix match for layer 3