## Slide 1: Network Processors: Motivation And Purpose
Lesson 11

## Slide 2: Second Generation Network Systems
Concurrent with ATM development (early 1990s)
Purpose: scale to speeds faster than single CPU capacity
Features
  – Use classification instead of demultiplexing
  – Decentralized architecture to offload CPU
  – Design optimized for fast data path

## Slide 3: Second Generation Network Systems (details)
Multiple network interfaces
  – Powerful NIC
  – Private buffer memory
High-speed hardware interconnects NICs
General-purpose processor only handles exceptions
Sufficient for medium speed interfaces (100 Mbps)

## Slide 4: Reminder: Protocol Processing In Second Generation Network Systems
NIC handles most of layers 1 - 3
Fast-path forwarding avoids CPU completely

## Slide 5: Third Generation Network Systems
Late 1990s
Functionality partitioned further
Additional hardware on each NIC
Almost all packet processing off-loaded from CPU

## Slide 6: Third Generation Design
NIC contains
  – ASIC hardware
  – Embedded processor plus code in ROM
NIC handles
  – Classification
  – Forwarding
  – Traffic policing
  – Monitoring and statistics

## Slide 7: Embedded Processor
Two possibilities
  – Complex Instruction Set Computer (CISC)
  – Reduced Instruction Set Computer (RISC)
RISC used often because
  – Higher clock rates
  – Smaller
  – Lower power consumption

## Slide 8: Purpose Of Embedded Processor In Third Generation Systems
Third generation systems use an embedded processor to handle layer 4 functionality and exception packets that cannot be forwarded across the fast path. An embedded processor architecture is chosen because ease of implementation and amenability to change are more important than speed.

## Slide 9: Protocol Processing In Third Generation Systems
Special-purpose ASICs handle lower layer functions
Embedded (RISC) processor handles layer 4
CPU only handles low-demand processing

## Slide 10: Are Third Generation Systems Sufficient?

## Slide 11: Are Third Generation Systems Sufficient?
Almost

## Slide 12: Are Third Generation Systems Sufficient?
Almost . . . but not quite.

## Slide 13: Problems With Third Generation Systems
High cost
Long time to market
Difficult to simulate/ test
Expensive and time-consuming to change
  – Even trivial changes require silicon respin
  – 18-20 month development cycle
Little reuse across products
Limited reuse across versions

## Slide 14: Problems With Third Generation Systems (continued)
No consensus on overall framework
No standards for special-purpose support chips
Requires in-house expertise (ASIC designers)

## Slide 15: A Fourth Generation
Goal: combine best features of first generation and third generation systems
  – Flexibility of programmable processor
  – High speed of ASICs
Technology called network processors

## Slide 16: .Definition Of A Network Processor
A network processor is a special-purpose, programmable hardware device that combines the low cost and flexibility of a RISC processor with the speed and scalability of custom silicon (i.e., ASIC chips). Network processors are building blocks used to construct network systems.

## Slide 17: Network Processors: Potential Advantages
Relatively low cost
Straightforward hardware interface
Facilities to access
  – Memory
  – Network interface devices
Programmable
Ability to scale to higher
  – Data rates
  – Packet rates

## Slide 18: Network Processors: Potential Advantages
Relatively low cost
Straightforward hardware interface
Facilities to access
  – Memory
  – Network interface devices
Programmable
Ability to scale to higher
  – Data rates
  – Packet rates

## Slide 19: The Promise Of Programmability
For producers
  – Lower initial development costs
  – Reuse software in later releases and related systems
  – Faster time-to-market
  – Same high speed as ASICs
For consumers
  – Much lower product cost
  – Inexpensive (firmware) upgrades

## Slide 20: Choice Of Instruction Set
Programmability alone insufficient
Also need higher speed
Should network processors have
  – Instructions for specific protocols?
  – Instructions for specific protocol processing tasks?
Choices difficult

## Slide 21: Instruction Set
Need to choose one instruction set
No single instruction set best for all uses
Other factors
  – Power consumption
  – Heat dissipation
  – Cost
More discussion later in the course

## Slide 22: Scalability
Two primary techniques
  – Parallelism
  – Data pipelining
Questions
  – How many processors?
  – How should they be interconnected?
More discussion later

## Slide 23: Costs And Benefits Of Network Processors
Currently
  – More expensive than conventional processor
  – Slower than ASIC design
Where do network processors fit?
  – Somewhere in the middle

## Slide 24: Achieving Higher Speed
What is known
  – Must partition packet processing into separate functions
  – To achieve highest speed, must handle each function with separate hardware
What is unknown
  – Exactly what functions to choose
  – Exactly what hardware building blocks to use
  – Exactly how building blocks should be interconnected

## Slide 25: Variety Of Network Processors
Economics driving a gold rush
  – NPs will dramatically lower production costs for network systems
  – A good NP design potentially worth lots of $$
Result
  – Wide variety of architectural experiments
  – Wild rush to try yet another variation

## Slide 26: An Interesting Observation
System developed using ASICs
  – High development cost ($1M)
  – Lower cost to replicate
System developed using network processors
  – Lower development cost
  – Higher cost to replicate
Conclusion: amortized cost favors ASICs for most high-volume systems

## Slide 27: Summary
Third generation network systems have embedded processor on each NIC
Network processor is programmable chip with facilities to process packets faster than conventional processor
Primary motivation is economic
  – Lower development cost than ASICs
  – Higher processing rates than conventional processor