## Slide 1: Protocol Software On A Conventional Processor
Lesson 7

## Slide 2: Possible Implementations Of Protocol Software
In an application program
  – Easy to program
  – Runs as user-level process
  – No direct access to network devices
  – High cost to copy data from kernel address space
  – Cannot run at wire speed

## Slide 3: Possible Implementations Of Protocol Software (continued)
In an embedded system
  – Special-purpose hardware device
  – Dedicated to specific task
  – Ideal for stand-alone system
  – Software has full control

## Slide 4: Possible Implementations Of Protocol Software (continued)
In an embedded system
  – Special-purpose hardware device
  – Dedicated to specific task
  – Ideal for stand-alone system
  – Software has full control
  – You will experience this in lab!

## Slide 5: Possible Implementations Of Protocol Software (continued)
In an operating system kernel
  – More difficult to program than application
  – Runs with kernel privilege
  – Direct access to network devices

## Slide 6: Interface To The Network
Known as Application Program Interface (API)
Can be
  – Asynchronous
  – Synchronous
Synchronous interface can use
  – Blocking
  – Polling

## Slide 7: Asynchronous API
Also known as event-driven
Programmer
  – Writes set of functions
  – Specifies which function to invoke for each event type
Programmer has no control over function invocation
Functions keep state in shared memory
Difficult to program
Example: function f () called when packet arrives

## Slide 8: Synchronous API Using Blocking
Programmer
  – Writes main flow-of-control
  – Explicitly invokes functions as needed
  – Built-in functions block until request satisfied
Example: function wait_for_packet() blocks until packet arrives
Easier to program

## Slide 9: Synchronous API Using Polling
Nonblocking form of synchronous API
Each function call returns immediately
  – Performs operation if available
  – Returns error code otherwise
Example: function try_for_packet() either returns next packet or error code if no packet has arrived
Closer to underlying hardware

## Slide 10: Typical Implementations And APIs
Application program
  – Synchronous API using blocking (e.g., socket API)
  – Another application thread runs while an application blocks
Embedded systems
  – Synchronous API using polling
  CPU dedicated to one task
Operating systems
  – Asynchronous API
  – Built on interrupt mechanism

## Slide 11: Example Asynchronous API
Design goals
  – For use with network processor
  – Simplest possible interface
  – Sufficient for basic packet processing tasks
Includes
  – I/ O functions
  – Timer manipulation functions

## Slide 12: Example Asynchronous API (continued)
Initialization and termination functions
  – on_startup()
  – on_shutdown()
Input function (called asynchronously)
  – recv_frame()
Output functions
  – new_fbuf()
  – send_frame()

## Slide 13: Example Asynchronous API (continued)
Timer functions (called asynchronously)
  – delayed_call()
  – periodic_call()
  – cancel_call()
Invoked by outside application
  – console_command()

## Slide 14: Processing Priorities
Determine which code CPU runs at any time
General idea
  – Hardware devices need highest priority
  – Protocol software has medium priority
  – Application programs have lowest priority
Queues provide buffering across priorities

## Slide 15: Priorities
Lowest Priority
  Applications
Medium Priority
  Protocol Processing
Highest Priority
  Device drivers
  Handling frames

## Slide 16: Implementation Of Priorities In An Operating System
Two possible approaches
  – Interrupt mechanism
  – Kernel threads

## Slide 17: Interrupt Mechanism
Built into hardware
Operates asynchronously
Saves current processing state
Changes processor status
Branches to specified location

## Slide 18: Two Types Of Interrupts
Hardware interrupt
  – Caused by device (bus)
  – Must be serviced quickly
Software interrupt
  – Caused by executing program
  – Lower priority than hardware interrupt
  – Higher priority than other OS code

## Slide 19: Software Interrupts And Protocol Code
Protocol stack operates as software interrupt
When packet arrives
  – Hardware interrupts
– Device driver raises software interrupt
When device driver finishes
  – Hardware interrupt clears
  – Protocol code is invoked

## Slide 20: Kernel Threads
Alternative to interrupts
Familiar to programmer
Finer-grain control than software interrupts
Can be assigned arbitrary range of priorities

## Slide 21: Conceptual Organization
Packet passes among multiple threads of control
Queue of packets between each pair of threads
Threads synchronize to access queues

## Slide 22: Possible Organization Of Kernel Threads For Layered Protocols
One thread per layer
One thread per protocol
Multiple threads per protocol
Multiple threads per protocol plus timer management thread(s)
One thread per packet

## Slide 23: One Thread Per Layer
Easy for programmer to understand
Implementation matches concept
Allows priority to be assigned to each layer
Means packet is enqueued once per layer

## Slide 24: One Thread Per Protocol
Like one thread per layer
  – Implementation matches concept
  – Means packet is enqueued once per layer
Advantages over one thread per layer
  Easier for programmer to understand
  – Finer-grain control
  – Allows priority to be assigned to each protocol

## Slide 25: Multiple Threads Per Protocol
Further division of duties
Simplifies programming
More control than single thread
Typical division
  – Thread for incoming packets
  – Thread for outgoing packets
  – Thread for management/ timing

## Slide 26: Timers And Protocols
Many protocols implement timeouts
  – TCP
    * Retransmission timeout
    * 2MSL timeout
  – ARP
    * Cache entry timeout
– IP
* Reassembly timeout

## Slide 27: Multiple Threads Per Protocol Plus Timer Management Thread(s)
Observations
– Many protocols each need timer functionality
– Each timer thread incurs overhead
Solution: consolidate timers for multiple protocols

## Slide 28: Is One Timer Thread Sufficient?
In theory
– Yes
In practice
  – Large range of timeouts (microseconds to tens of seconds)
  – May want to give priority to some timeouts
Solution: two or more timer threads

## Slide 29: Multiple Timer Threads
Two threads usually suffice
Large-granularity timer
  – Values specified in seconds
  – Operates at lower priority
Small-granularity timer
  – Values specified in microseconds
  – Operates at higher priority

## Slide 30: Thread Synchronization
Thread for layer i
  – Needs to pass a packet to layer i + 1
  – Enqueues the packet
Thread for layer i + 1
  – Retrieves packet from the queue

## Slide 31: Thread Synchronization
Thread for layer i
  – Needs to pass a packet to layer i + 1
  – Enqueues the packet
Thread for layer i + 1
  – Retrieves packet from the queue
Context switch required!

## Slide 32: Context Switch
OS function
CPU passes from current thread to a waiting thread
High cost
Must be minimized

## Slide 33: One Thread Per Packet
Preallocate set of threads
Thread operation
  – Waits for packet to arrive
  – Moves through protocol stack
  – Returns to wait for next packet
Minimizes context switches

## Slide 34: Summary
Packet processing software usually runs in OS
API can be synchronous or asynchronous
Priorities achieved with
  – Software interrupts
  – Threads
Variety of thread architectures possible