## Slide 1: An Example ACE
Lesson 25

## Slide 2: We Will
Consider an ACE
Examine all the user-written code
See how the pieces fit together

## Slide 3: Choice Of Network System
Used to demonstrate
  – Basic concepts
  – Code structure and organization
Need to
  – Minimize code size and complexity
  – Avoid excessive detail
  – Ignore performance optimizations

## Slide 4: The Example
Trivial network system
In-line paradigm using two ports
  – Ethernet-to-Ethernet connectivity
  – Known as bump-in-the-wire
Count Web packets
  – Frame carries IP
  – Datagram carries TCP
  – Destination port is 80
Named WWBump ( Web Wire Bump )

## Slide 5: WWBump
Passes all traffic in either direction
Counts Web packets

## Slide 6: Design
Code written for bridal veil testbed
Accepts input from either port zero or port one
Forwards incoming traffic to opposite port
Uses the ingress and egress library ACEs supplied by Intel
Defines a wwbump MicroACE
Passes each Web packet to the core component (exception)
Provides access to current packet count via the crosscall
Uses an ixsys.config file to specify binding of targets

## Slide 7: Static ACE Data Structure
Intel software requires
  – Static control block for ACE
  – Structure is named ( ix_ace )
Programmer can add additional fields to control block

## Slide 8: Fields In The Wwbump Control Block
Field Type Purpose
name string Name of the ACE in ixsys.config
tag int ID of ACE assigned by Resource
Manager
ue int Bitmask of microengines running the ACE
bname string TAG name that the microblock uses
ccbase ix_base_t Handle for crosscall service

## Slide 9: Example Declarations (wwbump.h)
/* wwbump.h -- global constants and declarations for wwbump */
#ifndef __WWBUMP_H
#define __WWBUMP_H
#include <ix/asl.h>
#include <ix/microace/rm.h>
#include <ix/asl/ixbasecc.h>
#include <wwbump_import.h>
typedef struct wwbump wwbump;
struct wwbump
{
ix_ace ace; /* Mandatory handle for all ACEs */
char name[128]; /* Name of this ACE given in ixsys.config */
int tag; /* ID assigned by RM for SA-to-ME communic. */
int ue; /* Bitmask of MEs this MicroACE runs on */
char bname[128]; /* Block name (need .import_var $bname_TAG) */
ix_base_t ccbase; /* Handle for cross call service */
};
/* Exception handler prototype */
int exception(void *ctx, ix_ring r, ix_buffer b);
#endif /* __WWBUMP_H */

## Slide 10: Shared Symbolic Constants
Core component programmed in C
Microblock component programmed in assembly language
Typical trick: bracket lines of code with #ifndef to prevent multiple instantiations
Unusual trick
  – Both languages share C-preprocessor syntax
  – Can place all constant definitions in shared file

## Slide 11: Distinguishing Code At Compile Time
Preprocessor can distinguish
  – Code for core component
  – Code for microblock component
Technique: symbolic constant MICROCODE only defined when assembling microcode
Can use #ifdef

## Slide 12: Example File Of Symbolic Constants (wwbump_import.h)
/* wwbump_import.h -- define or import tag for wwbump MicroACE */
#ifndef _WWBUMP_IMPORT_H
#define _WWBUMP_IMPORT_H
#ifdef MICROCODE
.import_var WWBUMP_TAG
#else
#define WWBUMP_TAG_STR "WWBUMP_TAG"
#endif
#endif /* _WWBUMP_IMPORT_H */

## Slide 13: Division Of Microcode Into Files
Two main files
Follow Intel naming convention: macro and file names related to microcode start with uppercase letter
WWBump.uc
  – Code for packet processing
  – Defines macro WWBump
WWB_dl.uc
  – Contains code for dispatch loop

## Slide 14: WWBump Macro
Performs two functions
  – Specifies eventual output port for packet
  – Classifies the packet
Classification
  – Represented as disposition
    StrongARM (exception)
    Next microblock (Egress)
  Stored in register dl_next_block

## Slide 15: WWBump Details
Uses Intel ingress macro
Calls DL_GetInputPort to determine input port (0 or 1)
Calls DL_SetOutputPort to specify output port
When passing packet to core component
  – Set exception to WWBUMP_TAG
  – Set return code to IX_EXCEPTION

## Slide 16: Steps WWBump Takes During Classification
Read packet header into six SDRAM transfer registers
Check
  – Ethernet type field (0800 16 )
  – IP type field (6)
  – TCP destination port (80)
Difficult (ugly) in microcode
  – Must use IP header length to calculate port offset
  – Port number is 16 bits; transfer register is 32

## Slide 17: File WWBump.uc (part 1)
/* WWBump.uc - microcode to process a packet */
#define ETH_IP 0x800 ; Ethernet type for IP
#define IPT_TCP 6 ; IP type for TCP
#define TCP_WWW 80 ; Dest. port for WWW
#macro WWBumpInit[]
/* empty because no initialization is needed */
#endm
#macro WWBump[]
xbuf_alloc[$$hdr,6] ; Allocate 6 SDRAM registers
/* Reserve a register (ifn) and compute the output port for the */
/* frame; a frame that arrives on port 0 will go out port 1, and */
/* vice versa */
.local ifn
DL_GetInputPort[ifn] ; Copy input port number to ifn
alu [ ifn, ifn, XOR, 1 ] ; XOR with 1 to reverse number
DL_SetOutputPort[ifn] ; Set output port for egress
.endlocal

## Slide 18: File WWBump.uc (part 2)
/* Read first 24 bytes of frame header from SDRAM */
.local base off
Buf_GetData[base, dl_buffer_handle] ; Get the base SDRAM address
DL_GetBufferOffset[off] ; Get packet offset in bytes
alu_shf[off, --, B, off, >>3] ; Convert to Quad-words
sdram[read, $$hdr0, base, off, 3], ctx_swap ; Read 3 Quadwords
; (six registers)
.endlocal
/* Classify the packet. If any test fails, branch to NotWeb# */
/* Verify frame type is IP (1st two bytes of the 4th longword) */
.local etype
immed[etype, ETH_IP]
alu_shf[ --, etype, -, $$hdr3, >>16] ; 2nd operand is shifted
br!=0[NotWeb#]
.endlocal
/* Verify IP type is TCP (last byte of the 6th longword) */
br!=byte[$$hdr5, 0, IPT_TCP, NotWeb#]

## Slide 19: File WWBump.uc (part 3)
/* Verify destination port is web (offset depends on IP header size */
.local base boff dpoff dport
/* Get length of IP header (3rd byte of 4th longword), and */
/* convert to bytes by shifting by six bits instead of eight */
ld_field_w_clr[dpoff, 0001, $$hdr3, >>6] ; Extract header length
/* Mask off bits above and below the IP length */
.local mask
immed[mask, 0x3c] ; Mask out upper and lower 2 bits
alu [ dpoff, dpoff, AND, mask ]
.endlocal

## Slide 20: File WWBump.uc (part 4)
/* Register dpoff contains the IP header length in bytes. Add */
/* Ethernet header length (14) and offset of the destination */
/* port (2) to obtain offset from the beginning of the packet */
/* of the destination port. Add to SDRAM address of buffer, */
/* and convert to quad-word offset by dividing by 8 (shift 3). */
alu[dpoff, dpoff, +, 16] ; Add Ether+TCP offsets
Buf_GetData[base, dl_buffer_handle] ; Get buffer base address
DL_GetBufferOffset[boff] ; Get data offset in buf.
alu[boff, boff, +, dpoff] ; Compute byte address
alu_shf[boff, --, B, boff, >>3] ; Convert to Q-Word addr.
sdram[read, $$hdr0, base, boff, 1], ctx_swap ; Read 8 bytes
/* Use lower three bits of the byte offset to determine which */
/* byte the destination port will be in. If value >= 4, dest. */
/* port is in the 2nd longword; otherwise it’s in the first. */
alu[ dpoff, dpoff, AND, 0x7 ] ; Get lowest three bits
alu[ --, dpoff, -, 4] ; Test and conditional
br>=0[SecondWord#] ; branch if value >=4

## Slide 21: File WWBump.uc (part 5)
FirstWord#: /* Load upper two bytes of register $$hdr0 */
ld_field_w_clr[dport, 0011, $$hdr0, >>16] ; Shift before mask
br[GotDstPort#] ; Check port number
SecondWord#: /* Load lower two bytes of register $$hdr1 */
ld_field_w_clr[dport, 0011, $$hdr1, >>16] ; Shift before mask
GotDstPort#: /* Verify destination port is 80 */
.local wprt
immed[wprt, TCP_WWW] ; Load 80 in reg. wprt
alu[--, dport, -, wprt] ; Compare dport to wprt
br!=0[NotWeb#] ; and branch if not equal
.endlocal
.endlocal

## Slide 22: File WWBump.uc (part 6)
IsWeb#: /* Found a web packet, so send to the StrongARM */
/* Set exception code to zero (we must set this) */
.local exc ; Declare register exc
immed[exc, 0] ; Place zero in exc and
DL_SetExceptionCode[exc] ; set exception code
.endlocal
/* Set tag core component’s tag (required by Intel macros) */
.local ace_tag ; Declare register ace_tag
immed32[ace_tag, WWBUMP_TAG] ; Place wwbump tag in reg.
DL_SetAceTag[ace_tag] ; and set tag
.endlocal
/* Set register dl_next_block to IX_EXCEPTION to cause dispatch */
/* to pass packet to StrongARM as an exception */
immed[dl_next_block, IX_EXCEPTION] ; Store return value
br[Finish#] ; Done, so branch to end
NotWeb#: /* Found a non-web packet, so forward to next microblock*/
immed32[dl_next_block, 1] ; Set return code to 1

## Slide 23: File WWBump.uc (part 7)
Finish#: /* Packet processing is complete, so clean up */
xbuf_free[$$hdr] ; Release xfer registers
#endm

## Slide 24: Dispatch Loop Algorithm
initialize dispatch loop macros;
do forever {
if (packet has arrived from the StrongARM)
Send the packet to egress microblock;
if (packet has arrived from Ethernet port) {
Invoke WWBump macro to process the packet;
if (return code specifies exception) {
Send packet to StrongARM;
} else {
Send packet to egress microblock;
}
}
}

## Slide 25: Dispatch Loop Code
Contained in file WWB_dl.uc
Not defined as separate macro
Includes several files
  – Standard (Intel) header files to define basic macros
  – Our packet processing macro (file WWBump.uc)

## Slide 26: File WWB_dl.uc (part 1)
/* WWB_dl.uc - dispatch loop for wwbump program */
/* Constants */
#define IX_EXCEPTION 0 ; Return value to raise an exception
#define SA_CONSUME_NUM 31 ; Ignore StrongARM packets 30 of 31 times
#define SEQNUM_IGNORE 31 ; StrongARM fastport sequence num
/* Register declarations (as required for Intel dispatch loop macros) */
.local dl_reg1 dl_reg2 dl_reg3 dl_reg4 dl_buffer_handle dl_next_block
/* Include files for Intel dispatch loop macros */
#include "DispatchLoop_h.uc"
#include "DispatchLoopImportVars.h"
#include "EthernetIngress.uc"
#include "wwbump_import.h"
/* Include the packet processing macro defined previously */
#include "WWBump.uc"

## Slide 27: File WWB_dl.uc (part 2)
/* Microblock initialization */
DL_Init[]
EthernetIngress_Init[]
WWBumpInit[]
/* Dispatch loop that runs forever */
.while(1)
Top_Of_Loop#: /* Top of dispatch loop (for equivalent of C continue) */
/* Test for a frame from the StrongARM */
DL_SASource[ ] ; Get frame from SA
alu[--, dl_buffer_handle, -, IX_BUFFER_NULL] ; If no frame, go test
br=0[Test_Ingress#], guess_branch ; for ingress frame
br[Send_MB#] ; If frame, go send it
Macro DLSAsource
  – Checks for packets from StrongARM
  – Returns one packet after SA_CONSUME_NUM calls

## Slide 28: File WWB_dl.uc (part 3)
Test_Ingress#: /* Test for an Ethernet frame */
EthernetIngress[ ] ; Get an Ethernet frame
alu[--, dl_buffer_handle, -, IX_BUFFER_NULL] ; If no frame, go back
br=0[Top_Of_Loop#] ; to start of loop
/* Check if ingress frame valid and drop if not */
br!=byte[dl_next_block, 0, 1, Drop_Packet#]
/* Invoke WWBump macro to set output port and classify the frame */
WWBump[]
/* Use return value from WWBump to dispose of frame: */
/* if exception, jump to code that sends to StrongARM */
/* else jump to code that sends to egress */
alu[ --, dl_next_block, -, IX_EXCEPTION] ; Return code is exception
br=0[Send_SA#] ; so send to StrongARM
br[Send_MB#] ; Otherwise, send to next microblock
Note dl_next_block specifies whether the frame should be treated as an exception or forwarded to next microblock

## Slide 29: File WWB_dl.uc (part 4)
Send_SA#:
/* Send the frame to the core component on the StrongARM as an */
/* exception. Note that tag and exception code are assigned by */
/* the microblock WWBump. */
DL_SASink[ ]
.continue ; Continue dispatch loop
Send_MB#:
/* Send the frame to the next microblock (egress). Note that the */
/* output port (field oface hidden in the internal structure) has */
/* been assigned by microblock WWBump. */
DL_MESink[ ]
nop
.continue
Drop_Packet#:
/* Drop the frame and start over getting a new frame */
DL_Drop[ ]
.endw
nop ; Although the purpose of these no-ops is
nop ; undocumented, Intel examples include them.
nop
.endlocal

## Slide 30: Code For Core Component
Written in C
Defines two basic functions
  – Exception handler called when packet arrives from StrongARM
  – Default action called when another frame arrives (e.g., from another ACE)

## Slide 31: Exception Handler
Function named exception
Receives packets from microblock
Must call Intel function RmGetExceptionCode
Can call Intel function RmSendPacket to forward packet to a microblock
Three arguments
  – Pointer to ACE control block
  – Ring buffer (not used in our code)
  – Pointer to ix_buffer holding packet

## Slide 32: Default Action
Function named ix_action_default
Required part of every ACE
Called when frame arrives from source other than microblock component
Our version merely discards the packet
Code in file action.c

## Slide 33: File action.c (part 1)
/* action.c -- Core component of wwbump that handles exceptions */
#include <wwbump.h>
#include <stdlib.h>
#include <wwbcc.h>
ix_error exception(void *ctx, ix_ring r, ix_buffer b)
{
struct wwbump *wwb = (struct wwbump *) ctx; /* ctx is the ACE */
ix_error e;
unsigned char c;
(void) r; /* Note: not used in our example code */
/* Get the exception code: Note: Intel code requires this step */
e = RmGetExceptionCode(wwb->tag, &c);
if ( e ) {
fprintf(stderr, "%s: Error getting exception code", wwb->name);
ix_error_dump(stderr, e);
ix_buffer_del(b);
return e;
}
Call to RmGetExceptionCode is required

## Slide 34: File action.c (part 2)
Webcnt++; /* Count the packet as a web packet */
/* Send the packet back to wwbump microblock */
e = RmSendPacket(wwb->tag, b);
if ( e ) { /* If error occurred, report the error */
ix_error_dump(stderr, e);
ix_buffer_del(b);
return e;
}
return 0;
}
First line of this page
  – Performs entire ‘‘work’’ of exception handler
  – Increments global counter ( Webcnt )
Once packet has been counted, RmSendPacket enqueues packet back to microblock group

## Slide 35: File action.c (part 3)
/* A core component must define an ix_action_default function that is */
/* invoked if a frame arrives from the core component of another ACE. */
/* Because wwbump does not expect such frames, the version of the */
/* default function used with wwmbump simply deletes any packet that */
/* it receives via this interface. */
int ix_action_default(ix_ace * a, ix_buffer b)
{
(void) a; /* This line prevents a compiler warning*/
ix_buffer_del(b); /* Delete the frame */
return RULE_DONE; /* This step required */
}
Code for default action is trivial: discard any packet that arrives

## Slide 36: Initialization And Finalization
Additional code needed for each ACE
Function ix_init performs initialization
  – Allocates memory for the ACE control block
  – Invokes Intel macros
    ix_ace_init for internal initialization
    RmInit to form connection to Resource Manager
    RmRegister to register with Resource Manager

## Slide 37: Initialization And Finalization (continued)
Function ix_fini performs finalization
  – Invokes Intel macros
    cc_fini to terminate crosscalls
    RmTerm to terminate Resource Manager
    ix_ace_fini to deallocate ACE control block

## Slide 38: File init.c (part 1)
/* init.c -- Initialization and completion routines for the wwbump ACE */
#include <stdlib.h>
#include <string.h>
#include <wwbump.h>
#include <wwbcc.h>
/* Initialization for the wwbump ACE */
ix_error ix_init(int argc, char **argv, ix_ace ** ap)
{
struct wwbump *wwb;
ix_error e;
(void)argc;
/* Set so ix_fini won’t free a random value if ix_init fails */
*ap = 0;
/* Allocate memory for the WWBump structure (includes ix_ace) */
wwb = malloc(sizeof(struct wwbump));
if ( wwb == NULL )
return ix_error_new(IX_ERROR_LEVEL_LOCAL, IX_ERROR_OOM, 0,
"couldn’t allocate memory for ACE");

## Slide 39: File init.c (part 2)
/* Microengine mask is always passed as the third argument */
wwb->ue = atoi(argv[2]);
/* Set blockname used to associate the ACE with its microblock */
strcpy(wwb->bname, "WWBUMP");
/* The name of the ACE is always the 2nd argument */
/* The first argument is the name of the executable */
wwb->name[sizeof(wwb->name) - 1] = ’\0’;
strncpy(wwb->name, argv[1], sizeof(wwb->name) - 1);
/* Initializes the ix_ace handle (including dispatch loop, control */
/* access point, etc) */
e = ix_ace_init(&wwb->ace, wwb->name);
if (e) {
free(wwb);
return ix_error_new(0,0,e,"Error in ix_ace_init()\n");

## Slide 40: File init.c (part 3)
/* Initialize a connection to the resource manager */
e = RmInit();
if (e) {
ix_ace_fini(&wwb->ace);
free(wwb);
return ix_error_new(0,0,e,"Error in RmInit()\n");
}
/* Register with the resource manager (including exception handler) */
e = RmRegister(&wwb->tag, wwb->bname,&wwb->ace, exception, wwb, wwb->ue);
if (e) {
RmTerm();
ix_ace_fini(&wwb->ace);
free(wwb);
return ix_error_new(0,0,e,"Error in RmRegister()\n");
}

## Slide 41: File init.c (part 4)
/* Initialize crosscalls */
e = cc_init(wwb);
if ( e ) {
RmUnRegister(&wwb->tag);
RmTerm();
ix_ace_fini(&wwb->ace);
free(wwb);
return e;
}
*ap = &wwb->ace;
return 0;
}
ix_error ix_fini(int argc, char **argv, ix_ace * ap)
{
struct wwbump *wwb = (struct wwbump *) ap;
ix_error e;
(void)argc;
(void)argv;
/* ap == 0 if ix_init() fails */
if ( ! ap )
return 0;

## Slide 42: File init.c (part 5)
/* Finalize crosscalls */
e = cc_fini(wwb);
if ( e )
return e;
/* Unregister the exception handler and microblocks */
e = RmUnRegister(wwb->tag);
if ( e )
return ix_error_new(0,0,e,"Error in RmUnRegister()\n");
/* Terminate connection with resource manager */
e = RmTerm();
if ( e )
return ix_error_new(0,0,e,"Error in RmTerm()\n");
/* Finalize the ix_ace handle */
e = ix_ace_fini(&wwb->ace);
if ( e )
return ix_error_new(0,0,e,"Error in ix_ace_fini()\n");
/* Free the malloc()ed memory */
free(wwb);
return 0;
}

## Slide 43: The Important Point
Wwbump performs a trivial task
The code invokes Intel’s ingress and egress ACEs
The code is written using Intel’s dispatch loop macros
The code is large.

## Slide 44: The Important Point
Wwbump performs a trivial task
The code invokes Intel’s ingress and egress ACEs
The code is written using Intel’s dispatch loop macros
The code is huge!

## Slide 45: An Example Crosscall
Trivial example
  – Provide access to current Web packet count
  – Wwbump ACE acts as crosscall server
  – Only exports one function
  – Can be called from non-ACE program
Exported function named getcnt

## Slide 46: Basic Steps When Building A Crosscall Facility
Define a set of functions that the crosscall server exports
Create an Interface Definition Language ( IDL ) declaration for each function, and use the IDL compiler to generate the corresponding stub code
Write code for each exported function with arguments that match the generated stub arguments
Write an initialization function
Write a finalization function

## Slide 47: Example IDL Specification
interface wwbump
{
twoway long getcnt();
};
IDL specification declares
  – Name and type of exported function
  – Type of each argument

## Slide 48: Files Generated By The IDL Compiler
File Contents Description
IFACE_stub_c.h Crosscall data types and types for
initialization and finalization functions
IFACE_intName Interface name as a string
IFACE_FCN_opName Function name as a string
stub_IFACE_init() Client crosscall initialization
stub_IFACE_fini() Client crosscall finalization
IFACE_FCN_fptr Function pointer for FCN
stub_IFACE_FCN() Client-side crosscall function
CC_VMT_IFACE Crosscall Virtual Method Table structure
deferred_cb_IFACE_IFCN() Client callback prototype
IFACE_FCN_cb_fptr Client callback function pointer
CB_VMT_IFACE Client callback VMT
getCBVMT_IFACE() Find VMT for callback
IFACE_sk_c.h Declarations of server-side interfaces
sk_IFACE_init() Server initialization
sk_IFACE_fini() Server finalization
getCCVMT_IFACE() Find the VMT for the interface
invoke_IFACE_IFCN() Invoke a crosscall
IFACE_stub_c.h Included file

## Slide 49: More Files Generated By The IDL Compiler
File Contents Description
IFACE_cc_c.h Prototypes for individual crosscall functions
IFACE_FCN() Prototype for function FCN
IFACE_sk_c.h Included file
IFACE_cb_c.h Prototypes and Virtual Method Tables
for client-side callback functions
IFACE_FCN_cb() Prototype for client callback
IFACE_stub_c.h Included file
IFACE_stub_c.c Code for client-side initialization and
finalization crosscall functions
IFACE_sk_c.c Code for server-side initialization and
finalization and VMT accessor functions
IFACE_cc_c.h Prototypes for individual crosscall functions
IFACE_FCN() Prototype for function FCN
IFACE_sk_c.h Included file
IFACE_cb_c.h Prototypes and Virtual Method Tables
for client-side callback functions
IFACE_FCN_cb() Prototype for client callback
IFACE_stub_c.h Included file

## Slide 50: Even More IDL-Generated Files
File Description
IFACE_cc_c.c Default code for crosscall functions
that merely return an error.
IFACE_cb_c.c Default implementations of client callback
functions that merely return an error.

## Slide 51: Code For A (Trivial) Crosscall Server
Programmer must supply
  – Code for exported function(s)
  Initialization function
  – Finalization function
  – Global variable declarations
  – Code to change pointer(s) in global virtual method table
Example code in file wwbcc.c

## Slide 52: File wwbcc.c (part 1)
/* wwbcc.c -- wwbump crosscall functions */
#include <stdlib.h>
#include <string.h>
#include <wwbump.h>
#include <wwbcc.h>
#include "wwbump_sk_c.h"
#include "wwbump_cc_c.h"
long Webcnt; /* Stores the count of web packets */
/* Initialization function for the crosscall */
ix_error cc_init(struct wwbump *wwb)
{
CC_VMT_wwbump *vmt = 0;
ix_cap *capp;
ix_error e;
/* Initialize an ix_base_t structure to 0 */
memset(&wwb->ccbase, 0, sizeof(wwb->ccbase));
/* Get the OMS communications access point (CAP) of the ACE */
ix_ace_to_cap(&wwb->ace, &capp);

## Slide 53: File wwbcc.c (part 2)
/* Invoke the crosscall initialization function and check for error */
e = sk_wwbump_init(&wwb->ccbase, capp);
if (e)
return ix_error_new(0,0,e,"Error in sk_wwbump_init()\\n");
/* Retarget incoming crosscalls to our getcnt function */
/* Get a pointer to the CrossCall Virtual Method Table */
e = getCCVMT_wwbump(&wwb->ccbase, &vmt);
if (e)
{
sk_wwbump_fini(&wwb->ccbase);
return ix_error_new(0,0,e,"Error in getCCVMT_wwbump()\\n");
}
/* Retarget function pointer in the table to getcnt */
vmt->_pCC_wwbump_getcnt = getcnt;
/* Set initial count of web packets to zero */
Webcnt = 0;
return 0;
}

## Slide 54: File wwbcc.c (part 3)
/* Cross call termination function */
ix_error cc_fini(struct wwbump *wwb)
{
ix_error e;
/* Finalize crosscall and check for error */
e = sk_wwbump_fini(&wwb->ccbase);
if ( e )
return ix_error_new(0,0,e,"Error in sk_wwbump_fini()\\n");
return 0; /* If no error, indicate sucessful return */
}
/* Function that is invoked each time a crosscall occurs */
ix_error getcnt(ix_base_t* bp, long* rv)
{
(void)bp; /* Reference unused arg to prevent compiler warnings */
/* Actual work: copy the web count into the return value */
*rv = Webcnt;
/* Return 0 for success */
return 0;
}

## Slide 55: Tying It All Together
Need to specify
  – ACEs to be loaded
  – Which ACEs are ingress / egress
  – Number and speed of network ports
Configuration file used
  – Named ixsys.config
  – Programmer usually modifies sample file

## Slide 56: Configuration Examples
file 0 /mnt/SlowIngressWWBump.uof
Defines file /mnt/lowIngressWWBump.uof to be
  – Ingress microcode (type 0)
  Associated with slow ports (10/100 ports)

## Slide 57: Configuration Examples (continued)
microace wwbump /mnt/wwbump none 0 0
Specifies
  – wwbump is a microace
  – Runs on the ingress side (first zero)
  – Has unknown type (second zero)

## Slide 58: Configuration Examples (continued)
    bind static ifaceInput/default wwbump
    bind static wwbump/default ifaceOutput
Specifies
  – Default binding for ingress ACE is wwbump
  – Default binding for output from wwbump is ACE named ifaceOutput

## Slide 59: Configuration Examples (continued)
    sh command
Specifies command to be run on the StrongARM
Typical use: preload ARP cache
sh arp -s 10.1.0.2 01:02:03:04:05:06

## Slide 60: Summary
A huge amount of low-level code is required, even for a trivial ACE that counts Web packets or a trivial crosscall that returns the contents of an integer. In addition to the code, a detailed configuration file must be created to specify bindings among ACEs.