## Slide 1: Overview Of The Intel® IXA Network Processors
Lesson 17

## Slide 2: An Example Network Processor
We will
  – Choose one example
  – Examine the hardware
  – Gain first-hand experience with software
The choice: Intel

## Slide 3: Intel Network Processor Terminology
Intel® Internet Exchange Architecture (Intel® IXA)
  Broad reference to architecture
  – Both hardware and software
  – Control plane and data plane
Intel® IXA Network Processor
  – Network processor that implements Intel® IXA

## Slide 4: Intel® IXP1200
Name of first generation Intel® Network Processor chip
Four models available
Model Pin Support Support Possible Clock
Number Count For CRC For ECC Rates (in MHz)
Intel® IXP1200 432 no no 166, 200, or 232
Intel® IXP1240 432 yes no 166, 200, or 232
Intel® IXP1250 520 yes yes 166, 200, or 232
Intel® IXP1250 520 yes yes 166 only
Differences in speed, power consumption, packaging
Term Intel® IXP1200 refers to any model

## Slide 5: Intel® IXP1200 Features
One embedded RISC processor
Six programmable packet processors
Multiple, independent onboard buses
Processor synchronization mechanisms
Small amount of onboard memory
One low-speed serial line interface
Multiple interfaces for external memories
Multiple interfaces for external I/ O buses
A coprocessor for hash computation
Other functional units

## Slide 6: Intel® IXP1200 External Connection Speeds
Type Bus Width Clock Rate Data Rate
Serial line (NA) (NA) 38.4 Kbps
PCI bus 32 bits 33-66 MHz 2.2 Gbps
IX bus 64 bits 66-104 MHz 4.4 Gbps
SDRAM bus 64 bits ≤ 232 MHz 928.0 MBps
SRAM bus 16 or 32 bits ≤ 232 MHz 464.0 MBps
Note: MBps abbreviates Mega Bytes per second

## Slide 7: Intel® IXP1200 Internal Units
Quantity Component Purpose
1 Embedded RISC processor Control, higher layer protocols,
and exceptions
6 Packet processing engines I/O and basic packet processing
1 SRAM access unit Coordinate access to the
external SRAM bus
1 SDRAM access unit Coordinate access to the
external SDRAM bus
1 IX bus access unit Coordinate access to the
external IX bus
1 PCI bus access unit Coordinate access to the
external PCI bus
several Onboard buses Internal control and data transfer

## Slide 8: Intel® IXP1200 Internal Architecture

## Slide 9: Processors On The Intel® IXP1200
Processor Type Onboard? Programmable?
General Purpose Processor no yes
Embedded RISC Processor yes yes
Microengines yes yes
Coprocessors yes no
Physical Interfaces no no

## Slide 10: Intel® IXP1200 Memory Hierarchy
Memory Maximum On Typical
Type Size Chip? Use
GP Registers 128 regs. yes Intermediate computation
Inst. Cache 16 Kbytes yes Recently used instructions
Data Cache 8 Kbytes yes Recently used data
Mini Cache 512 bytes yes Data that is reused once
Write buffer unspecified yes Write operation buffer
Scratchpad 4 Kbytes yes IPC and synchronization
Inst. Store 64 Kbytes yes Microengine instructions
FlashROM 8 Mbytes no Bootstrap
SRAM 8 Mbytes no Tables or packet headers
SDRAM 256 Mbytes no Packet storage

## Slide 11: Intel® IXP1200 Memory Characteristics
Memory Addressable Relative Special
Type Data Unit (bytes) Access Time Features
Scratch 4 12 - 14 synchronization via
test-and-set and other
bit manipulation,
atomic increment
SRAM 4 16 - 20 queue manipulation,
bit manipulation,
read/write locks
SDRAM 8 32 - 40 direct transfer path
to I / O devices

## Slide 12: Memory Addressability
Each memory specifies minimum addressable unit
  – SRAM organized into 4-byte words
  – SDRAM organized into 8-byte longwords
Physical address refers to word or longword
Examples
  – SDRAM address 1 refers to bytes 8 through 15
  – SRAM address 1 refers to bytes 4 through 7

## Slide 13: Summary
We will use Intel Intel® IXP1200 as example
Intel® IXP1200 offers
  – Embedded processor plus parallel packet processors
  – Connections to external memories and buses