## Slide 1
The Windows™ Telephony API
Toby Nixon
Program Manager
Desktop and Business Systems Division
Microsoft Corporation
tnixon@microsoft.com

## Slide 2
We don’t need to tell you why CTI is important anymore, do we?

## Slide 3
TAPI Objectives
Flexible
Portable - connection model and network independent
Sharable - multiple app support
Media aware
Extensible
Familiar programming model
Usability features
See my article in April ‘96 IEEE Communications Magazine

## Slide 4
Integration Models
Add-in board or
motherboard
Voice modem
Proprietary set

## Slide 5
LAN-Based Server
LAN
(control only)
Desktop
CTI Link
Audio/Data
Trunks
Switch/network

## Slide 6
Integrated Server/Switch
LAN
(control only)
Desktop
Trunks

## Slide 7
Single Wire to Desktop (ATM, IsoEthernet)
LAN
(control and
audio/data)
Desktop
Trunks

## Slide 8
Architecture
Windows Telephony DLL
Application programming interface
Service Provider interface
Phone-enabled applications
Rolodex
Call control
Agent desktop
Mail
Conferencing
PBX
Cellular
POTS
PCS
ISDN
Telephone network services

## Slide 9
Benefits
Application developers
  Standard gives critical market mass
  Lets developers focus on value-added, not plumbing
Telephone network, switch, hardware providers
  Let others write compatible applications
  Applications expand the market for telephone services
Customers
  Protects software investment and provides future compatibility
  Wide variety of software is cost-effective
  Permits integration of a multivendor world
  Insist on open standards

## Slide 10
Line Device Class
Wirepair, channel... a path to the switch
Logically terminate at the API even though may not physical terminate in the PC
One or more addresses are associated with a line (“call appearances”)
Usually one active call at any time per line, but some lines support multiple calls
API allows access to multiple lines
  Ability to carry on simultaneous conversations
  Line capabilities need not be the same

## Slide 11
Phone Device Class
Abstraction of phone set elements
  Hookswitch audio I/O devices
    Handset, speaker, headset
  Ringer
  Display
  Buttons and lamps
  Download areas
API provides query and manipulation of a phone’s elements
Allows local audio input and output

## Slide 12
Telephony Services
Assisted Telephony
Full Telephony
Basic Services
Supplementary Services
Extended Services

## Slide 13
Assisted Telephony
Service
Provider
Full
Telephony
Application
Call
Manager
Application
Telephony-
enabled
Application
TAPI
Request Queue
Service
Provider
Service
Provider

## Slide 14
WordBasic Macro
Declare Function tapiRequestMakeCall Lib "TAPI32"
(number$, appName$, calledParty$, comment$) As Long
Sub MAIN
n$ = Selection$()
retval = tapiRequestMakeCall(n$,"Word 95","","")
If retval <> 0 Then
Beep
b$ = "Your request to dial "
+ Chr$(34) + n$ + Chr$(34)
+ " failed."
MsgBox b$, "Dialing Failed", 48
End If
End Sub

## Slide 15
Basic Services
Initialization and shutdown
Version negotiation
Opening and closing lines
Capabilities
Device status
Configuration

## Slide 16
Basic Services
Address translation
Making calls
Call states and events
Answering calls
Dropping calls
Call handle manipulation
Assisted telephony server

## Slide 17
Supplementary Services
Hold
Transfer
Conference
Forward
Park
Pickup
Completion
Accept, redirect, reject

## Slide 18
Supplementary Services
Secure from interruptions
Generating digits and tones
Digit and tone monitoring
Media mode monitoring
Media stream routing and control
User-user info
Change call parameters
Phone terminal control

## Slide 19
Media Stream
Information stream carried over a call
Media stream accessed via separate Windows “media” API
  Some already defined (comm, wave, NDIS)
  Others being defined (fax, video conference)
Use TAPI to determine association between telephony and media devices
Service Provider may support multiple APIs

## Slide 20
Line as a Media Device
Telephony API
Wave API
Any wave
application
Integrated telephony
and wave application
(for example, answering
machine application)
Windows
Telephony SPI
Wave SPI
Combined telephony and wave
Service Provider

## Slide 21
Address Formats
“Canonical” format for use in address books
  Like ITU-T E.123: +1 (206) 882-8080
  Location independence
“Dialable” format includes all digits to be dialed, plus special functions
Dialing Properties maintains location information, dialing rules
Functions to do translation, display properties, update properties

## Slide 22
TAPI 1.4 (Windows 95)
Support for 32-bit applications
Plug ‘n’ Play
Common dialog for Dialing Properties
Access to country list
Get/Set application priorities
Provider-initiated conferences
Other capability/status extensions
Universal modem driver

## Slide 23
TAPI 2.0
Initially ships in Windows NT 4.0
Full 32-bit architecture designed for migration to future releases of “Windows 95” platform
Backwardly compatible with 16-bit TAPI applications
32-bit, Unicode service provider interface
API extensions in Windows NT 4.0
Client-server service provider and admin tools ship separately after NT 4.0

## Slide 24
Client-Server Telephony
Windows Telephony is the most flexible CTI architecture, supporting the greatest variety of connection and network models
TAPI has always supported client-server operation, from earliest design stages
Using TAPI does not require adding new hardware in the PC
Early implementation focus on supporting largest-volume platform and applications

## Slide 25
“Third Party Call Control”
Server applications can see all devices on the server - the essence of “third party” call control
Clients have a “first party” view of network
  Applications don’t have to deal with complexity of an API that forces a “third party” view on all users
Clients can also view and control any part of the network, if authorized
Service providers model switch resources (stations, dialers, queues, trunks, route points) as line devices

## Slide 26
Client-server TAPI Service Provider Architecture
TAPI DLL
TAPI DLL
Server
Client PC
Client PC
App
App
App
App
App
App
SPI
API
SPI
API
to switch
Stub
Stub
Service Provider (Server Part)
LAN

## Slide 27
Get it now!
TAPI-based Client-Server solutions are available now
  Windows 3.1/3.11 and Windows 95 clients
  A variety of back-end servers including Windows NT, OS/2, Unix
Several sources including Genesys, Dialogic, and others

## Slide 28
Client Block Diagram
16-bit TAPI
Application
TAPI.DLL
TAPI32.DLL
32-bit TAPI
Application
LRPC
TAPISRV.EXE
REMOTE TSP
RPC
WINSOCK2
TCP/IP
NDIS3
TSPUI DLL

## Slide 29
Server Block Diagram
TAPI32.DLL
Server
Application
LRPC
TAPISRV.EXE
PBX.TSP
RPC
WINSOCK2
TCP/IP
NDIS3
CSTA, ASAI, MITAI,
MeridianLink, etc.

## Slide 30
Call Center Features
ACD queues; agent login, state and activity monitoring and control
Predictive dialing
Routing
Call data
Call treatment
Message waiting and display control without using Phone functions

## Slide 31
Other TAPI 2.0 Features
TAPI message notification based on Win32 Event or Completion Port
UNICODE support
Transfer through hold, no-hold conference, on-step transfer
Centralized timing of call state duration and media events
Monitor single address
And more!

## Slide 32
We listened, and will continue listening, to your suggestions

## Slide 33
How Do I Get It?
TAPI 1.4 binaries built into Windows 95
TAPI 2.0 binaries built into Windows NT 4.0
SDK Integrated with Win32SDK in MSDN Developer Platform Level 2
  Headers, libs, sample source, docs
  Redistributable binaries for Windows 3.x

## Slide 34
Developer Support
Sign up for Microsoft Developer Support contract; call +1 (800) 936-3500
Peer support on CompuServe Windows™ Extensions Forum (GO WINEXT), Section 3
Email tapi@microsoft.com to register as a developer or other non-technical issues

## Slide 35
Questions?