## Slide 2
BROWSING Balan Sethu Raman Software Design Engineer Windows NT Development Microsoft Corporation
™

## Slide 3
TOPICS
Introduction
Server Interoperability
Client Interoperability

## Slide 4
BROWSING
A mechanism for discovering CIFS servers
A good browsing mechanism
  is immune to machine failures
  minimizes network traffic
  minimizes server discovery time
  minimizes change discovery latency

## Slide 5
Browser Architecture
Servers use mailslot messages to announce themselves
Each subnet has an independent browsing authority
  Some mailslot messages used for browsing are not propagated across subnet boundaries
Inter-subnet browsing uses Domain Master Browser Server (PDC)

## Slide 6
Browser Architecture
Master Browser Server coordinates browsing activities
Master Browser Server is dynamically elected rather than statically configured
Elections are conducted using mailslot messages
Each local subnet has its own Master Browser Server

## Slide 7
Browsing Infrastructure
For compatibility reasons the browsing architecture relies on NetBIOS names.
All browser messages are mailslot writes
The mailslot writes are shipped on the wire as Transact SMBs
  all browser data structures are shipped in the data portion of the Transact SMB

## Slide 8
NetBIOS names for browsing
NETBIOS Name Conventions
  16 characters long, last character has special significance.
  <NameString> [LastChar] represents a NetBIOS name obtained by taking the NameString and padding it with blanks upto 15 characters and inserting LastChar as the 16 th character

## Slide 9
NetBIOS names .. contd
<Computer Name> [0]
  unique name used for processing browing related requests , e.g., Get Backup List
<Domain Name> [1b]
  unique name added by the PDC and defended on the net
<Domain Name> [1d]
  local unique name added by a Master Browser.

## Slide 10
Mailslot Names
All browser messages directed at <Computer Name> [0] are sent to \mailslot\lanman
All browser messages directed at other NetBIOS names are sent to \mailslot\browse

## Slide 11
Non Browser Server
Preriodically announces itself with a directed mailslot message to a well known name
Announcement frequency decreases as the server stays up for longer periods
  Varies from one per minute to once every twelve minutes
Responds to requests for information from the master browser

## Slide 12
Browser Messages
Host Announcement
Announcement Request

## Slide 13
Announcement Message
struct BROWSE_ANNOUNCE_PACKET {
UCHAR BrowseType; // == 1
BROWSE_ANNOUNCE_PACKET_1
BrowseAnnouncement;
}

## Slide 14
Announcement Message
struct BROWSE_ANNOUNCE_PACKET_1 {
UCHAR UpdateCount;
ULONG Periodicity;
UCHAR ServerName[16];
UCHAR VersionMajor;
UCHAR VersionMinor;
ULONG Type;
USHORT BrowserConstants[2];
CHAR Comment[49];
}

## Slide 15
Announcement Message
UpdateCount
    changes every time host data changes
Periodicity
    announcment time interval in millisecond
Type
    bit vector signifying the srvices supported
BrowserConstants
    must be 0x415,0xaa55

## Slide 16
Request Announcement
struct REQUEST_ANNOUNCE_PACKET {
UCHAR Type; // always set to 2
REQUEST_ANNOUNCE_PACKET_1
RequestAnnouncement;
}

## Slide 17
Request Announcement
struct REQUEST_ANNOUNCE_PACKET_1 {
UCHAR Pad;
// Host to reply to
CHAR Send[16];
}

## Slide 18
Client Interoperability
A client obtains the list of servers by:
  sending a GetBackupList mailslot message to the <DomainName > [1d] and <Domain Name> [1b] and receiving a list of BackupBrowsers for the domain
  establishing an SMB session and tree connecting to IPC$ with one of them
  executing the NetServerEnum API

## Slide 19
BackupList Request Message
struct BACKUP_LIST_REQUEST_1 {
UCHAR RequestedCount;
ULONG Token;
}
struct BACKUP_LIST_REQUEST {
UCHAR Type;
BACKUP_LIST_REQUEST_1 BackupListRequest;
}

## Slide 20
BackupList Response Message
struct BACKUP_LIST_RESPONSE_1 {
UCHAR BackupServerCount;
ULONG Token;
UCHAR BackupServerList[1];
}
struct BACKUP_LIST_RESPONSE {
UCHAR Type;
BACKUP_LIST_RESPONSE_1 BackupListResponse;
}

## Slide 21
Remote Admin Protocol API
The param portion of the Transact request SMB includes
  descriptor of the params
  descriptor of the response expected
  marshalled params
The data and param portions of the Transact response contains the API results

## Slide 22
NetServerEnum API
Remote Admin Protocol API
  custom marshalling and unmarshalling
  predecessor to RPC
Two flavors
  NetServerEnum2
    64k buffer size limitation
  NetServerEnum3
    64k buffer size but continuable, not supported by all servers

## Slide 23
Questions?